## Slide 1
2015 World Radiocommunication Conference Agenda Items
Affecting EESS (active)
May 29, 2014
Committee On Radio Frequencies
Thomas vonDeak
NASA Spectrum Office
Notes: This presentation is a reflection of the collective efforts of the NASA Spectrum Office. Information regarding this office and its scope of activities can be found at: https://www.spacecomm.nasa.gov/spacecomm/programs/spectrum_management/about/default.cfm

## Slide 2: Overview
This presentation will provide a summary of the issues regarding the EESS (active) under these three World Radiocommunications Conference Agenda items:
  1.1: Additional mobile broadband spectrum requirements including IMT and the study of potential candidate frequency bands [dc to Daylight]
  1.6.1/1.6.2: Fixed-satellite service (E-s and s-E) of 250 MHz in the range between 10 GHz and 17 GHz
  Fixed-satellite service (E-s) of 250 MHz in Region 2 and 300 MHz in Region 3 within the range 13-17 GHz
  1.12: Extension of the current worldwide allocation to the EESS (active) in the frequency band 9 300-9 900 MHz by up to 600 MHz on a primary and/or secondary basis, as appropriate, within the frequency range 8 700 9 300 MHz and/or 9 900-10 500 MHz

## Slide 3: WRC-15 Agenda item 1.1
Mobile Service is seeking additional bandwidth for cellular and radio-Local Area Network (RLAN) operations.
No specific frequency bands have been identified under the agenda item resolution; however, the 5 350 – 5 470 MHz band is under consideration for RLAN operations.
  The RLAN community has proposed mitigation techniques and ITU-R WP 7C has reviewed the techniques and liaised its views to ITU-R JTG 4-5-6-7.

## Slide 4: Proposed Mitigation techniques
The following is a list and brief description of the RLAN mitigation techniques proposed by the RLAN community.
Geolocation Database
  A publically available global database containing the current orbital characteristics of all EESS (active) spacecraft as well as their current antenna pointing information would be accessed by the RLANs to determine when the RLANs should cease operation or move to another frequency.
Dynamic Frequency Selection (DFS)
  RLAN detection of the EESS (active) radar when the EESS (active) spacecraft is in the vicinity. Upon detection, the RLAN would cease transmitting or switch frequency of operation.
Sensors Network
  A distributed sensor network would be deployed by the RLAN to augment the RLAN deployment. This sensor network would provide advance information to the RLAN as to the presence of an EESS (active) spacecraft in the vicinity whereupon the RLAN would cease operation or switch frequency of operation.
Image post processing
  Post processing of the raw EESS data will remove the RLAN interference from the underlying desired data.
RLAN e.i.r.p. mask limiting
  RLAN implementation of an e.i.r.p. mask that would limit the power of an RLAN transmission directed towards a EESS spacecraft.
In addition, other mitigation techniques are being discussed for possible consideration or a combination of the above with other TBD techniques.

## Slide 5: ITU-R Working Party 7C views
Geolocation Database
  Database source issues: No organization exists that has a database of EESS (active) sensor orbital characteristics.
    NORAD (U.S. Stratcomm) nor the ITU Space Networks System is comprehensive enough.
  Oversight concerns: Maintenance of such a database would require international overview and will have to be developed and maintained by a suitable international organisation.
  One size doesn’t fit all: The orbital characteristics are different among different types of EESS (active) sensors (SAR, altimeters, scatterometers, ...).
  EESS antenna pointing: The instantaneous antenna pointing of the EESS (active) sensors is not available in any database nor is it likely to be made available by all EESS (active) operators.
  Many other concerns outside the expertise of WP 7C were expessed regarding this technique, such as hacking, IP tampering, and enforcement were also noted.

## Slide 6: ITU-R Working Party 7C views
Dynamic Frequency Selection (DFS)
  Latency problem: The detection would occur during an EESS (active) illumination of the area and interference to the EESS (active) would already have occurred. Regardless of the detection level used by the RLAN DFS this latency would render the technique ineffective in mitigating interference to the EESS (active) sensor.
Sensors Network
  Non-continuous SAR operations: SAR systems do not operate in a continuous manner and so when the sensor initiate operation may immediately encounter interference under this technique.
  RLAN sensors in the ocean?: Measurements on coastal areas would be impacted since it is unlikely that RLAN sensors would be deployed in open water.
  Sensor network latency: The speed of the EESS (active) sensor (7 km/sec) would require the RLAN sensor network to be prohibitively large and details describing the coordination of the RLAN sensor network and RLAN switch operation are absent.
  Enforcement: Enforcement of the proper operation of the sensor network is also a concern.

## Slide 7: ITU-R Working Party 7C views
Image post processing
  Never perfect: This technique always results in a reduction of its radiometric quality.
  Non-universal: The post-processing algorithms under study do not work for the case of interferometric SAR measurements.
  Single well behaved interferer dependent: Post-processing algorithms are only be effective when the interference is from a single source generating a coherent pulsed signal .
    RLAN interference seen by the SAR would be the composite of many different RLAN signals from multiple RLAN devices in the SAR footprint. These devices will not generate signals that are coherent among them.
RLAN e.i.r.p. mask limiting
  In theory an e.i.r.p. mask concept could work; however:
  Enforcement: Questions the means to correctly implement and enforce an e.i.r.p. mask
    Mass‑market unlicensed devices
    RLAN could be ceiling mounted or mounted in different manner (e.g. wall)
  Multipath: Also, a mask on indoor RLAN devices would not necessarily limit emissions towards the satellite
    Building multipath etc.

## Slide 8: Agenda item 1.6
Fixed Satellite Service (FSS) is seeking additional 250 MHz of uplink bandwidth in the frequency range of 13 - 17 GHz.
Although the entire 13 - 17 GHz range is under examination only two bands are plausibly viable for consideration: 13.4 - 13.75 GHz and 14.5. - 14.8 GHz.
  EESS (active) operates in the 13.4 -13.75 GHz band.
  The results of studies performed by NASA will be provided.

## Slide 9: Compatibility Analysis Input parameters
Relevant system characteristics
Victim receiver characteristics
  System noise, antenna pattern
Offending Transmitter characteristics
  Power, antenna gain and pointing, deployment characteristics
Link parameters
  Distance separation, shielding
Evaluation Criteria
Victim receiver acceptable limits of interference (Protection criteria)
  Amount of degradation to victim receiver signal that can be tolerated. (Interference to Noise ratio)
  Percentage of time the degradation can be tolerated.

## Slide 10: Compatibility Analysis Methods
Two basic types of analysis
Single entry Dynamic analysis
Remote Sensing System
Single
Fixed Satellite Service
uplink
Remote Sensing System
Global
Fixed Satellite Service
uplinks
Random
Systematic

## Slide 11: Compatibility Analysis Methods
Single entry, static
  Worst case (maximum power, minimum distance), main beam to main beam coupling of the offending receiver and the victim receiver is analyzed against the evaluation criteria.
  RESULTS: In general, if compatibility is found through this method then compatibility is ensured.
Dynamic analysis
  Dynamic analysis is undertaken when single entry static analysis indicates that compatibility is not ensured.
  Simulation of victim receiver and offending transmitter deployment using appropriate characteristics to evaluate the offending interference environment against both the amount of degradation to the victim receiver signal and the percentage of time that degradation can be tolerated.
RESULTS: In general, multiple studies produce multiple results due to different simulation assumptions used.

## Slide 12: Sea Surface Altimeter (SSALT)
All spacecraft are CNES (France) missions with NASA participation; plus radiometers
Launch Date: December 2001 (J1) and June 2008 (OSTM)
Polar orbit at 1336 km and 66° inclination with 10 day repeat
Polarization: Linear
RF Center Freq: 5300, 13575 MHz
RF bandwidth: 100, 320 MHz (C-band); 320 MHz (Ku-band)
Pulsewidth: 105.6 μsec
Pulse repetition freq: 1890-2310 Hz
Xmt Pwr: 16, 7 W Pk/3.9, 1.7 W Avg
Chirp rate: 0.9, 3.0 MHz/μsec
Transmit Duty Cycle: 24.4%
SSALTs are on JASON-1, -2(Ocean Surface Topology Mission),
This mission obtains measurements of ocean surface height using radar altimeter. OSTM is the Ocean Surface Topography Mission also known as JASON-2.

## Slide 13: Precipitation Radar on GPM
JAXA dual frequency Precipitation Radar instrument
Projected Launch Date: June 2014
Orbit at 407 km and 65° inclination
Polarization: N/A
RF Center Freq: 13.6 & 35.56 GHz
RF bandwidth: 14 MHz
Pulsewidth: 1.6 μsec
Pulse repetition freq: 4206 (Ku) & 4275 Hz (Ka)
Xmt Pwr: 1 kW (Ku) & 140 W Pk (Ka)/6.7 W (Ku) & 0.94 W (Ka) Avg
Chirp rate: 8.75 MHz/μsec
Transmit Duty Cycle: 0.67%
Global Precipitation Measurement (GPM) is a NASA/JAXA follow-on to TRMM
GPM concept centers on the deployment of a “Core” satellite carrying an advanced radar / radiometer system to measure precipitation from space and serve as a reference standard.

## Slide 14: Scatterometer on ISS ISS-RapidScat
NASA JPL QuikScat replacement
Projected Launch Date: June 2014
Orbit at 330-435 km and 51.65° inclination
Polarization: H(inner), V(outer)
RF Center Freq: 13.4 GHz
RF bandwidth: .53 MHz
Pulsewidth: 1 700 μsec
Pulse repetition freq: 180 Hz
Xmt Pwr: 80 W Pk
Chirp rate: 0.000311765 MHz/μsec
Transmit Duty Cycle: 30.6%
Ocean Wind Monitor on International Space Station
ISS-RapidScat will measure ocean surface wind speed and direction and help improve weather forecasts, including hurricane monitoring.

## Slide 15: Altimeter Characteristics: 13.25-13.75 GHz band
Mission | Altimeter |  |  |  | 
 | ENVISAT RA-2 | JASON-1/2 (OSTM) SSALT | HY-2A | JASON-3 (OSTM) SSALT | Sentinel-3 SRAL (Note 1)
Altitude, km | 764 | 1 336 | 963 | 1 336 | 814
Inclination, deg | 98.6 | 66 | 99.3 | 66 | 98.65
Ascending Node LST* | 10:30 | NSS | 06:00 | NSS | 22:00
Repeat period, days | 35 | 10 | 14 | 10 | 27
Antenna Diameter | 1.2m | 1.2m | 1.4m | 1.2m | 1.2m
Antenna Pk Xmt Gain, dBi | 41.2 | 42 | 43 | 43.2 | 42
Antenna Pk Rcv Gain, dBi | 41.2 | 42 | 43 | 43.2 | 42
Polarization | linear | linear | VV | linear | linear
Azimuth scan rate, rpm | 0 | 0 | 0 | 0 | 0
Antenna beam look angle, deg | 0 | 0 | 0 | 0 | 0
Antenna beam azimuth angle, deg | 0 | 0 | 0 | 0 | 0
Transmit Pk pwr, W | 60 | 25 | 20 | 25 | 7.1
e.i.r.p. peak, dBW | 59.0 | 56 | 56.0 | 56 | 50.5
Antenna elev. beamwidth, deg | 1.2 | 1.27 | 0.9 | 1.27 | 1.27
Antenna az. beamwidth, deg | 1.2 | 1.27 | 0.9 | 1.27 | 1.27
RF Center Frequency, MHz | 13575 | 13.575 | 13.580 | 13.575 | 13 575
RF bandwidth, MHz | 320,80,20 | 320 | 20, 80, 320 | 320 | 350
Pulsewidth, μsec | 20 | 106 | 102.4 | 106.0 | 49
Transmit Ave. pwr, W | 2.16 | 5.46 | 8.2 | 5.41 | 0.66
Pulse Repetition Frequency (PRF) Hz | 1795.33 | 2 060 | 1 000-4 000 | 2060 | 1 924 (LRM) - 17 825 (SAR mode)
Chirp rate, MHz/μsec | 16, 4, 1 | 3.02 | 0.2, 0.78, 3.12 | 3.02 | 7.14
Transmit duty cycle, % | 3.6 | 21.84 | 40.96 | 21.63 | 1.35-2.65, 9.31
e.i.r.p. ave, dBW | 44.5 | 49.37 | 52.1 | 49.33 | 40.2
System Noise figure, dB | 2.5 , 3.0 | 2.81 | [ ] | 2.6 | 3.1

## Slide 16: Scatterometer Characteristics: 13.25-13.75 GHz band
Mission | Scatterometer |  |  |  |  |  | 
 | QUICKSCAT SEAWINDS | HY-2A | OCEANSAT-2 | Scatsat-1 | Meteor-M | FY-3E WindRadar | RapidScat
Altitude, km | 803 | 963 | 720 | 720 | [ ] | 836 | 415
Inclination, deg | 98.6 | 99.3 | 98.28 | 98.28 | [ ] | [ ] | 51.65
Ascending Node LST | 06:00 | 06:00 | 12:00 | [ ] | 06:00 | 18:00 | [ ]
Repeat period, days | 4 | 14 | 2 | 2 | [ ] | [ ] | [ ]
Antenna Diameter | 1m | 1.3m | 1m | [ ] | [ ] | 1.4m x 0.2m | .75
Antenna Pk Xmt Gain, dBi | 41 | 42 | [ ] | [ ] | [ ] | 37.5 | 38
Antenna Pk Rcv Gain, dBi | 41 | 42 | [ ] | [ ] | [ ] | 37.5 | 38
Polarization | H (inner), V (outer) | HH, VV | HH, VV | [ ] | [ ] | HH,VV | H (inner), V (outer)
Azimuth scan rate, rpm | 18 | [ ] | 21.14 | [ ] | [ ] | [ ] | 18
Antenna beam look angle, deg | 40, 46 | [ ] | 43.63 (HH), 49.09 (VV) | [ ] | [ ] | 32-38 | 45,50.5
Antenna beam azimuth angle, deg | 0-360 | [ ] | [ ] | [ ] | [ ] | 0-360 | 0-360
Transmit Pk pwr, W | 100 | 120 | [ ] | [ ] | [ ] | 140 | 80
e.i.r.p. peak, dBW | 61.0 | 62.8 | [ ] | [ ] | [ ] | [ ] | 57
Antenna elev. beamwidth, deg | 1.6 | 1 | 1.67 | [ ] | [ ] | 6 | 2.4/2.2
Antenna az. beamwidth, deg | 1.6 | 1 | 1.47 | [ ] | [ ] | 0.8 | 2.1
RF Center Frequency, MHz | 13.402 | 13.255.5 | 13.515 | 13.515 | 13.500 | 13 350 | 13.4
RF bandwidth, MHz | 0.53 | 3-6 | 0.4 | [ ] | [ ] | [ ] | 0.53
Pulsewidth, μsec | 1 700 | 650-1200 | 1 350 | [ ] | [ ] | [ ] | 1 700
Transmit Ave. pwr, W | 30.6 | 28.8 | [ ] | [ ] | [ ] | [ ] | [ ]
Pulse Repetition Frequency (PRF) Hz | 180 | 100-200 | 200 | [ ] | [ ] | [ ] | 180
Chirp rate, MHz/μsec | 0.000311765 | 0.005 | [ ] | [ ] | [ ] | [ ] | 0.000311765
Transmit duty cycle, % | 30.6 | 24 | [ ] | [ ] | [ ] | [ ] | 30.6
e.i.r.p. ave, dBW | 55.9 | 56.6 | [ ] | [ ] | [ ] | [ ] | [ ]
System Noise figure, dB | 3.4 | [ ] | [ ] | [ ] | [ ] | [ ] | 3.4 dB
NOTE: RapidScat is a payload on the International Space Station.

## Slide 17: Precipitation Radar Characteristics: 13.25-13.75 GHz band
Mission | Precipitation radar |  |  | 
 | TRMM PR | CPM PMR | GPM DPR | CPM PMR2
Altitude, km | 350 | 410 | 407 | 400/6001
Inclination, deg | 35 | [ ] | 65 | 50
Ascending Node LST* | NSS | NSS | NSS | NSS
Repeat period, days | 23 | [ ] | [ ] | 
Antenna Diameter | 2.1m | 2m | 1.6m | 5.3m
Antenna Pk Xmt Gain, dBi | 47.7 | 47 | 47.4 | 55
Antenna Pk Rcv Gain, dBi | 47.7 | 47 | 47.4 | 55
Polarization | H | HH | [ ] | HH,HV
Azimuth scan rate, rpm | 0.197 | [ ] | [ ] | 
Antenna beam look angle, deg | 0-17 | ± 20 | ± 17 | ± 31
Antenna beam azimuth angle, deg | 0-17 | 0 | 0 | 0
Transmit Pk pwr, W | 578 | 1 000 | 1 000 | [ ]
e.i.r.p. peak, dBW | 75.3 | [ ] | 77.4 | [ ]
Antenna elev. beamwidth, deg | 0.71 | 0.7 | 0.7 | 0.28
Antenna az. beamwidth, deg | 0.71 | 0.7 | 0.7 | 0.28
RF Center Frequency, MHz | 13.7963, 13.802 | 13 650 | 13.600 | 13.6
Number of Beams | [ ] | [ ] | [ ] | 4
RF bandwidth, MHz | 0.6 | [ ] | 14 | 8x4
Pulsewidth, μsec | 1.60, 1.60 | 1.6 | 1.6 | 40
Transmit Ave. pwr, W | 2.57 | [ ] | 6.7 | [ ]
Pulse Repetition Frequency (PRF) Hz | 2776 | [ ] | 4 206 | [ ]
Chirp rate, MHz/μsec | ** | [ ] | 8.75 | [ ]
Transmit duty cycle, % | 0.44 | [ ] | 0.67 | [ ]
e.i.r.p. ave, dBW | 51.8 | [ ] | 55.7 | [ ]
System Noise figure, dB | 5.5 | [ ] | [ ] | 3.5

## Slide 18: Evaluation Criteria
Sensor type | Interference criteria |  | Data availability criteria (%) | 
 | Performance degradation | I/N (dB) | Systematic | Random
Synthetic aperture radar | 10% degradation of standard deviation of pixel power | –6 | 99 | 95
Altimeter | 4% degradation in height noise | –3 | 99 | 95
Scatterometer | 8% degradation in measurement of normalized radar backscatter to deduce wind speeds | –5 | 99 | 95
Precipitation radar | 7% increase in minimum rainfall rate | –10 | N/A | 99.8
Cloud profile radar | 10% degradation in minimum cloud reflectivity | –10 | 99 | 95
Recommends 2
that the interference and data availability criteria given in Table 2 be applied for instruments used for active sensing of the Earth’s land, oceans and atmosphere.
TABLE 2
Recommendation ITU-R RS.1166-4
Performance and interference criteria for active spaceborne sensors
NOTES:
Altimeter, Scatterometer, and Precipitation Radar operate in the 13.25-13.75 GHz band. Synthetic aperture radar and cloud profile radar do not operate in this band.
Systematic data availability is in regards to the data availability of a particular measurement area of interest.
Random data availability is in regards to the overall data availability; that is, the availability over the repeat period of the sensor.
Systematic data availability criteria doesn’t apply to precipitation radar.

## Slide 19: Analysis Results
Static Analysis:
Worst case analysis: main-beam-to-main-beam coupling of the FSS (E-s) transmitter and the EESS (active) receiver
  RESULTS: Emissions of the FSS (E-s) exceed the interference threshold criteria for all three EESS (active) sensors considered.
Dynamic Analysis (random data avail. criteria)
Parametric analysis conducted over the EESS (active) repeat period. Global FSS (E-s) deployment density varied from 1 (current) to 5 (worst case future).
  RESULTS: Compatibility is achieved for a FSS deployment density of 1 to 3.

## Slide 20: Analysis Results
Dynamic Analysis
(systematic data avail. criteria)
Evaluation of interference to a specific measurement area of interest. Using the USDA reservoir and lake monitoring program as a model, parametric studies were conducted varying the measurement area size, and the latitude deployment.
RESULTS: Single earth station uplinks would exceed the systematic data availability criteria. Small earth stations would exceed over the range of +/- 10 degrees latitude. Large earth stations would exceed over the range of +/- 45 latitude.

## Slide 21: Agenda item 1.12
EESS (active) is seeking an additional 600 MHz adjacent to the 9 300 -9 900 MHz band.
  This will enable high resolution SAR imagery and improve resistance to interference and weather.
Draft CPM Report text completed by ITU-R WP 7C at its May, 2014 meeting
  Three methods have been put forward to address the agenda item.
  All methods have the following conditions:
  The three methods will be summarized.

## Slide 22: AI 1.12 Methods
All three methods have the following conditions:
Systems operating in the new EESS (active) allocation would not cause harmful interference to nor claim protection from radars in the radio determination service.
The use of the extension band would be limited to EESS (active) systems requiring a bandwidth of more than 600 MHz.
Radio astronomy would be protected by a Recommendation incorporated by reference into the Radio Regulations.

## Slide 23: Methods A1 and A2
A1: Add a primary allocation to EESS (active) in the frequency band 9 900 – 10 500 MHz.
  Subject to the three conditions.
A2: Add a primary allocation to EESS (active) in the frequency band 9 900 – 10 500 MHz subject to inclusion of technical and regulatory constraints into the RRs.
  Subject to the three conditions.
  The protection of the Fixed Service (terrestrial microwave links) is to be ensured through a footnote in the RR with a pfd-limit.

## Slide 24: Method B
Primary EESS (active) allocation in the frequency bands 9 200 – 9 300 MHz and 9 900 – 10 400 MHz.
  Subject to the three conditions
  NASA prefers this method as the new allocation would be further away from the Deep Space (space-Earth) allocation in the 8 400 – 8 450 MHz band.

## Slide 25
FINI