## Slide 1
Title: Report on U.S. and CITEL Preparations for WRC-15
Preparer: Wayne A. Whyte Presenter: John E. Zuzek
Date: May 13, 2015 – Committee on Radio Frequencies (CORF)

## Slide 2: The “WRC Cycle”
Conference Preparatory Meeting (CPMYY-1)
Identifies Responsible, Contributing and Interested groups responsible to conduct technical studies addressing WRC-YY Agenda Items
3ish Years of:
Study by Responsible & Contributing Groups
Developing National & Multi-national Views, Positions, and Proposals
Conference Preparatory Meeting (CPMYY-2)
Creates Report of Study Results and Possible Regulatory Methods to Resolve Agenda Items
Radiocommunication Assembly (RA-YY)
Elects Chairs/Vice-Chairs for next WRC Study Cycle
Finalizes any remaining Recommendations/Reports resulting from Studies
Five-and-a-half weeks
World Radiocommunication Conference-XX
~20+ “Agenda Items” Renegotiated
“Agenda Items” for WRC-YY Decided
You are almost here…

## Slide 3: Key International Organizations
International Telecommunication Union (ITU)
  Specialized Agency of the United Nations (UN)
  Parallel with some more well known agencies including: IMF, ICAO, UNESCO, WHO, WMO
Inter-American Telecommunication Commission (CITEL)
  Agency of the Organization of American States
  Pre-coordinate Inter-American treaty level proposals going to ITU
Space Frequency Coordination Group (SFCG)
  29 Member, non-Military, Civil Space Agencies including: NASA, ESA, JAXA, CNES, RFSA, & CNSA
  Pre-coordination of spectrum for missions and treaty level proposals related to space science

## Slide 4: Working Group established within PCC.II
Chair: Uruguay, Hector Bude
(hbude@ursec.gub.uy)
Vice-Chair: United States of America, Carmelo Rivera (Carmelo.Rivera@doc.gov)
Recent and future meetings
  23-27 February 2015, Medellin, Colombia
  17-21 August 2015, Ottawa, Canada

## Slide 5: WRC Working Group Structure
Sub WG | Title | Agenda items | Coordinator
SGT1 | Mobile & Fixed | 1.1, 1.2, 1.3 | Mr. Marco Antonio ESCALANTE GUATEMALA
SGT2 | Radiolocation, Amateur, Maritime & Aeronautical | 1.4, 1.5, 1.15, 1.16, 1.17, 1.18 | Mr. Jonathan WILLIAMS UNITED STATES OF AMERICA
SGT3 | Space Science & MSS | 1.10, 1.11, 1.12, 1.13, 1.14, 1.9.2, 9.1.1 | Mr. Tarcisio BAKAUS BRAZIL
SGT4 | FSS & Satellite Regulatory | 1.6.1, 1.6.2, 1.7, 1.8, 1.9.1, 7, 9.1, 9.1.2, 9.1.3, 9.1.5, 9.1.8, 9.1*, 9.2*, 9.3 *Satellite issues | Mr. Jerry CONNER UNITED STATES OF AMERICA
SGT5 | General Regulatory, Future Work & Other | 2, 4, 8, 9.1.4, 9.1.6, 9.1.7, 9.2*, 10 *Non-satellite issues | Mr. Carmelo RIVERA UNITED STATES OF AMERICA

## Slide 6: INTER – AMERICAN PROPOSALS : DEFINITIONS
PRELIMINARY VIEWS (PV): an informal statement that the Administration is considering possible Preliminary Proposals on specific themes.
PRELIMINARY PROPOSAL (PP): a proposal that a CITEL Member State presents to PCC II with the purpose to turning it into an Inter-American Proposal and that has not been supported by another Member State.
DRAFT INTER-AMERICAN PROPOSAL (DIAP): PRELIMINARY PROPOSAL that has been supported by at least one other Member State.
INTER-AMERICAN PROPOSAL (IAP): DRAFT INTER-AMERICAN PROPOSAL (DIAP) for which the PCC II has ended its consideration and discussion, has been supported by at least six Members States and is not opposed by more than 50% of the number of supports obtained.

## Slide 7: Agenda Item 1.1: IMT/terrestrial mobile broadband Status of the Preliminary Proposals, Draft Inter-American Proposals and Inter-American Proposals (1 of 3)
Frequency Range (MHz) | MOD Mobile allocation in Article 5 | NOC
410-450 |  | DIAP BLZ/CHL/CTR/MEX/USA
470-698 |  | IAP1 ARG/B/CHI/DOM/SLV/EQA/GTM/NCG/PNR/PRG/PRU/URG
470-608, (NOC 608-614) | DIAP CAN/USA/MEX | 
614-698 | DIAP CAN/USA/MEX/CLM | 
1164-1215, 1215-1300, 1559-1610 |  | DIAP CAN/USA/GTM/MEX
1300-1400 |  | DIAP USA/CHL
1. Discussions have not ended.

## Slide 8: Agenda Item 1.1: IMT/terrestrial mobile broadband Status of the Preliminary Proposals, Draft Inter-American Proposals and Inter-American Proposals (2 of 3)
Frequency Range (MHz) | MOD Mobile allocation in Article 5 | NOC
1427-1518 | IAP B/CHL/CLM/CTR/DOM/USA/GTM/ MEX/PRU/URG | 
1427-1452 Mandatory OOBE on IMT | IAP B/CHL/CLM/CTR/DOM/GTM/MEX/ PRU/URG | 
1559-1610 |  | DIAP CAN/USA
2025-2110, 2200-2290 |  | DIAP MEX/USA/CAN/BLZ
2700-2900 |  | DIAP CHL/USA/GTM
3300-3400 | PP CLM | 

## Slide 9: Agenda Item 1.1: IMT/terrestrial mobile broadband Status of the Preliminary Proposals, Draft Inter-American Proposals and Inter-American Proposals (3 of 3)
Frequency Range (MHz) | MOD Mobile allocation in Article 5 | NOC
3400-3600 | DIAP B/CLM/CTR/EQA: MS with IMT identification | 
3400-4200 | DIAP (3400-3700 w/NOC above) CAN/USA | IAP BEL/BOL/SLV/MEX/NCG/PNR
3600-4200 |  | DIAP B/CTR/EQA/VEN
4400-4990 |  | PP USA
4500-4800 |  | IAP ARG/B/BOL/CHL/GTM/NCG/ MEX/PNR/SLV/URG/VEN
5850-6425 |  | IAP B/BLZ/CTR/GTM/MEX/NCG/ PNR/SLV

## Slide 10: Agenda Item 1.5: UAS - Satellite
DIAP (USA/MEX) supports CPM Method A – Use of the Fixed Satellite Service by unmanned aircraft for control and non-payload communications links (CNPC). Provides a footnote allowing the use of UAS CNPC links in the fixed-satellite service not subject to Appendices 30, 30A and 30B.
  ITU-R is responsible for determining the technical and regulatory conditions that will ensure interference-free operation of FSS links to mobile UAS platforms
  ICAO has the responsibility to develop the link performance standards and to determine if a particular link can be used by unmanned aircraft in particular airspace. Those standards are not yet complete.

## Slide 11: Agenda Item 1.6.1: FSS (E-s/s-E) 250 MHz in Region 1 in 10-17 GHz
1.6.1 DIAP (B/CAN/MEX/URG) supporting FSS (E-s) in 14.5-14.8 GHz in Region 1. SRS (E-s) upgraded to co-primary with FSS (E-s) that not part of broadcasting-satellite feederlinks.
U.S. does not yet have a position

## Slide 12: Agenda Item 1.6.2: FSS (E-s) 250 MHz in Region 2 and 300 MHz in Region 3 in 13-17 GHz
1.6.2 IAP (B/CAN/MEX/NCG/SLV/URG) supporting FSS (E-s) in 14.5-14.8 GHz. SRS (E-s) upgraded to co-primary with FSS (E-s) that are not part of broadcasting-satellite feederlinks.
U.S. does not yet have a position

## Slide 13: Agenda Item 1.9.1: FSS 7 150 – 7 250 MHz (s-E) and 8 400 – 8 500 MHz (E-s)
DIAP (CAN/MEX/USA) supporting NOC to 7150-7250 MHz and 8400-8500 MHz. Operational coordination with SRS in 7 GHz represents unacceptable burden on SRS operators. Very large exclusion zones around SRS ground stations would be needed in 8 GHz.

## Slide 14: Agenda Item 1.9.2: MMSS 7 375-7 750 MHz and 8 025-8 400 MHz
DIAP: CAN/USA
    NOC to Article 5
    SUP Resolution 758 (WRC-12)
(No apparent support for MMSS allocation within CITEL)

## Slide 15: Agenda Item 1.10: MSS, including the satellite component for broadband applications, including IMT 22 GHz to 26 GHz
IAP:
B/CAN/CTR/GTM/MEX/URG/ USA
  NOC to Article 5
  SUP Resolution 234 (WRC-12)
(No apparent support for MSS allocation within CITEL)

## Slide 16: Agenda Item 1.11: EESS (E-s) 7-8 GHz
IAP: ARG/B/CAN/MEX/URG/USA
  MOD Article 5 to add EESS (Earth-to-space) in the 7 190-7 250 MHz band and divide the Table of Frequency Allocation at 7 190 MHz to clarify the allocation of services within the Table.
  MOD No. 5.460 - consequential to dividing the Table at 7 190 MHz
  MOD Article 21 Tables 21-2 and 21-3 – consequential
  MOD Appendix 7 Table 7b – consequential
  SUP Resolution 650 (WRC-12)
  No EESS GSO restriction

## Slide 17: Agenda Item 1.12: EESS (active) up to 600 MHz extension within 8 700-9 300 MHz and/or 9 900-10 500 MHz
IAP: CAN/CHL/CLM/GTM/MEX/ USA/URG
Proposes CPM Method A1 (Option 2)
  MOD Article 5 : The bands 9 900-10 500 MHz be allocated to the Earth Exploration-satellite (active) service with primary status
  MOD footnote No. 5.476A to protect the Radionavigation and Radiolocation services
  ADD footnote No. 5.XXX to ensure the newly allocated spectrum is used solely by high resolution EESS systems whose spectrum needs exceeds the existing EESS allocation in the 9 300-9 900 MHz band
  FN incorporating a Recommendation to protect RAS
  FN to allow transition period for amateur-satellite service in 10.45-10.5 GHz.
  SUP Resolution 651(WRC-12)

## Slide 18: Agenda Item 1.13: 5 km distance limitation for proximity operations by space vehicles in the SRS (s-s)
IAP: B/CAN/USA/GTM/MEX/URG
  MOD No. 5.268 to remove 5 km distance separation limit, and remove reference to “extra-vehicular activities”
  SUP Resolution 652 (WRC-12)
5.268 Use of the band 410-420 MHz by the space research service is limited to space-to-space communications with within 5 km of an orbiting, manned space vehicle. The power flux-density at the surface of the Earth produced by emissions from stations of extra-vehicular activities the space research service (space-to-space) in the band 410-420 MHz shall not exceed –153 dB(W/m2) for 0°    5°, ‑153 + 0.077 ( – 5) dB(W/m2) for 5°    70° and –148 dB(W/m2) for 70°    90°, where  is the angle of arrival of the radio-frequency wave and the reference bandwidth is 4 kHz. No. 4.10 does not apply to extra-vehicular activities. In this frequency band the space research (space-to-space) service shall not claim protection from, nor constrain the use and development of, stations of the fixed and mobile services. No. 4.10 does not apply. (WRC-9715)

## Slide 19: Agenda Item 1.14: Continuous reference time-scale - whether by the modification of UTC or some other method
DIAP: USA/[URG]
  MOD No. 1.14 – The Coordinated Universal Time (UTC) definition would now read: Time scale, based on the second (SI) and maintained by the Bureau International de Poids et Mesures (BIPM, that forms the basis for the coordinated dissemination of standard frequencies and time signals.
  MOD No. 2.5 – Consequential change
  MOD Article 59 – Consequential change
  ADD Resolution [AAA] – to establish January 1, 2022 as the date of entry into force of the modified provisions to provide a transition period for the elimination of leap seconds
  SUP Resolution 653

## Slide 20: Agenda Item 1.17: Wireless avionics intra-communications
IAP: ARG/B/CAN/CTR/CLM/DOM/EQA/GTM/ MEX/NCG/PNR/ SLV/USA/URG
  ADD footnote to the Table of Frequency Allocations (4 200-4 400 MHz) allowing the provision of wireless avionics intra-communications (WAIC)
  ADD footnote specifying that passive sensing in the Earth exploration-satellite and space research services may be allocated on a secondary basis (maintaining the current allowance of these services), and that no protection is afforded to these services

## Slide 21: Agenda Item 1.18: Radiolocation service for automotive applications in 77.5-78.0 GHz
PP: USA
  Support a primary allocation to the radiolocation service in the frequency band 77.5-78 GHz limited to short range radar surface applications, including automotive applications

## Slide 22: Agenda Item 9.1.1: Protection of COSPAS/SARSAT in 406-406.1 MHz
IAP: ARG/B/CAN/CHL/CLM/CTR/NCG/ USA/URG
  MOD Resolution 205 (WRC-12) to strongly recommend to administrations not to make new frequency assignments within the frequency bands 405.9-406.0 MHz and 406.1-406.2 MHz under the mobile and fixed services;

## Slide 23: Agenda Item 9.1.8: Regulatory aspects for nano- and picosatellites
DIAP: ARG/USA/URG
  Supports NOC to Articles 9 & 11, SUP Res 757 and no WRC-19 Agenda Item as any filing issues can be addressed under the existing Agenda Item 7 at a future WRC.

## Slide 24: Agenda Item 9.2: Difficulties and inconsistencies encountered in the application of the Radio Regulations
Clarification of the use of allocations to space research (deep space) in near-Earth applications (Re: interpretation of Nos. 5.460 and 5.465)
  NASA developed a U.S. contribution to the CPM (Document 36) proposing that this issue be addressed as part of AI 9.2 and has proposed two methods for addressing the issue in the RRs.
    Method A – Modify Article 4 to add a new paragraph describing the permitted use of SRS (deep space) allocations near the Earth.
    Method B – Consider possible change to definition for SRS (No. 1.55) and/or “deep space” (RR No. 1.177) to clarify support for deep space missions during near-Earth phases.
  Issue was sent to the SC which referred it to the CPM
  Letter sent by Chair SG-7 to Director, BR. Rancy has stated privately that this is not his issue to solve. BR has no difficulty with interpretation.

## Slide 25: Agenda Item 10: Agenda Items for Future Conferences
DIAP
DOM/USA/URG
  AI to consider upgrading METSAT allocation in 460-470 MHz
DIAP:
CHL/CLM/DOM/USA/URG
  to consider 5350-5470 MHz for wireless access use including RLANs (follow on to AI 1.1)
PP: CAN
  Suppress existing Resolution 808 (WRC-12) and replace it with a new Resolution for the WRC-18 agenda
Under development in U.S.
  WRC-23 AI on Space Weather (NOAA)
  WRC-23 AI on 40-50 MHz EESS (active) (NASA)

## Slide 26: 2nd Session of the Conference Preparatory Meeting for WRC-15 (CPM15-2)
CPM15-2 took place in Geneva, Switzerland from 23 March through 2 April 2015
The meeting was attended by 1502 registered participants (1284 present) from 85 Member States and many Sector Members.
In addition to the Draft CPM Report, another 179 contributions from Member States and Sector Members were considered.
The work resulted in a final version of the CPM Report – a whopping 862 pages!!!