## Slide 1: CRAF Position on WRC-19 Agenda Items Relevant to Radio Astronomy
Talayeh Hezareh - CRAF FM
Max Planck Institute for Radio astronomy
Bonn, Germany

## Slide 2
AI 1.2 | to consider in-band power limits for earth stations operating in the mobile-satellite service, meteorological-satellite service and Earth exploration-satellite service in the frequency bands 401-403 MHz and 399.9-400.05 MHz, in accordance with Resolution 765 [COM6/7] (WRC-15);
CRAF Position
RAS has a primary allocation in the 406.1 - 410 MHz and the effect of the power level of the emissions of the earth stations in the uplink operations in the nearby frequency bands 401-403 MHz and 399.9 - 400.05 MHz must be investigated to ensure the protection of RAS from the earth stations of the MSS.

## Slide 3
AI 1.3 | to consider possible upgrading of the secondary allocation to the meteorological-satellite service (space-to-Earth) to primary status and a possible primary allocation to the Earth exploration satellite service (space-to-Earth) in the frequency band 460-470 MHz, in accordance with Resolution 766 [COM6/8] (WRC-15);
CRAF Position
The frequency band 460-470 MHz may be sufficiently far away from the RAS allocation at 406.1-410 MHz. However, a generic attenuation simulation using the parameters available for the DCS operations will be useful to investigate the compatibility of these systems with RAS.

## Slide 4
AI 1.6 | to consider the development of a regulatory framework for non-GSO FSS satellite systems that may operate in the frequency bands 37.5-39.5 GHz (space-to-Earth), 39.5-42.5 GHz (space-to-Earth), 47.2-50.2 GHz (Earth-to-space) and 50.4-51.4 GHz (Earth-to-space), in accordance with Resolution 159 [COM6/18] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS and EESS (passive) allocations. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed with the RAS and EESS.

## Slide 5
AI 1.7 | to study the spectrum needs for telemetry, tracking and command in the space operation service for non-GSO satellites with short duration missions, to assess the suitability of existing allocations to the space operation service and, if necessary, to consider new allocations, in accordance with Resolution 659 [COM6/19] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS allocations in the 150.05 - 153.0 MHz and 406.1 - 410.0 MHz bands. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed with the RAS.

## Slide 6
AI 1.8 | to consider possible regulatory actions to support Global Maritime Distress Safety Systems (GMDSS) modernization and to support the introduction of additional satellite systems into the GMDSS, in accordance with Resolution 359 (Rev.WRC-15);
CRAF Position
As stated in Res. 359, the new GMDSS provider must provide protection of incumbent services in accordance with the Radio Regulations, including those in adjacent frequency bands, from harmful interference. CRAF supports the protection of the existing primary RAS allocation in the 1610.6 - 1613.8 MHz band. No action on the modernization of the GMDSS and no changes to the RR should be made unless [the RAS band is free from harmful interference and] acceptable sharing and compatibility criteria are developed with the RAS.

## Slide 7
AI 1.9.1 | regulatory actions within the frequency band 156-162.05 MHz for autonomous maritime radio devices to protect the GMDSS and automatic identifications system (AIS), in accordance with Resolution 362 [COM6/10] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS allocations in the 150.05-153.0 MHz band. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed with the RAS.

## Slide 8
AI 1.9.2 | modifications of the Radio Regulations, including new spectrum allocations to the maritime mobile-satellite service (Earth-to-space and space-to-Earth), preferably within the frequency bands 156.0125-157.4375 MHz and 160.6125-162.0375 MHz of Appendix 18, to enable a new VHF data exchange system (VDES) satellite component
CRAF Position
This is the AI 1.16 of WRC-15, which was postponed to WRC-19 due to the lack of sufficient studies. CRAF supported the Method C2 and C1 of the CPM15-2 report as long as an attenuation of 85 dB and the pfd mask described in section 3/1.16/4.3 of the report as proposed by the MMSS are implemented for the nearby radio astronomy band. Under such conditions compatibility between MMSS in the band 161.7875-161.9375 MHz and the RAS in the band 150.05-153 MHz will be feasible.

## Slide 9
AI 1.10 | to consider spectrum needs and regulatory provisions for the introduction and use of the Global Aeronautical Distress and Safety System (GADSS), in accordance with Resolution 426 [COM6/11] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS frequency allocations. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS from future GADSS operations.

## Slide 10
AI 1.11 | to take necessary actions, as appropriate, to facilitate global or regional harmonized frequency bands to support railway radiocommunication systems between train and trackside within existing mobile service allocations, in accordance with Resolution 236 [COM6/12] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS frequency allocations. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS from future railway radiocommunication systems.

## Slide 11
AI 1.12 | to take necessary actions, as appropriate, to facilitate global or regional harmonized frequency bands to support railway radiocommunication systems between train and trackside within existing mobile service allocations, in accordance with Resolution 236 [COM6/12] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS frequency allocations. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS from future ITS operations.

## Slide 12
AI 1.13 | to consider identification of frequency bands for the future development of International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution 238 [COM6/20] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS, SRS, and EESS (passive) frequency allocations. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS, SRS, and EESS (passive) from future IMT operations. A number of RAS and passive frequency bands, which may be affected by the future IMT allocations are listed in the Table below.

## Slide 13
Frequency Band (GHz) | RAS Status | RR Footnote
23.6-24.0 | PRI | 5.340
31.3-31.5 | PRI | 5.340
42.5-43.5 | PRI | 5.149
48.54-49.44 |  | 5.340, 5.149
50.2-50.4 |  | 5.340
76.0-77.0 | PRI | 5.149
81.0-86.0 | PRI | 5.149

## Slide 14
AI 1.14 | to consider, on the basis of ITU-R studies in accordance with Resolution 160 [COM6/21] (WRC- 15), appropriate regulatory actions for high-altitude platform stations (HAPS), within existing fixed- service allocations;
CRAF Position
The frequency band considered in Region 1 for studies regarding this agenda item is not of concern to CRAF. However, CRAF supports the RAS operations in other regions as well and requests compatibility studies to ensure the protection of RAS in Region 2 from unwanted emissions of HAPS links. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS.

## Slide 15
AI 1.15 | to consider identification of frequency bands for use by administrations for the land-mobile and fixed services applications operating in the frequency range 275-450 GHz, in accordance with Resolution 767 [COM6/14] (WRC-15);
CRAF Position
CRAF supports the protection of existing RAS, SRS, and EESS (passive) frequency allocations. CRAF also supports the development of propagation models for this frequency range. No changes should be made to the RR unless acceptable sharing and compatibility criteria are developed to ensure the protection of RAS, SRS, and EESS (passive) from future services and applications above 275 GHz.

## Slide 16: FURTHER ISSUES FOR CRAF
NGSO systems at 10.7-12.5 GHz (DL) and 14-14.5 GHz (UL) OneWeb
Iridium NEXT generation
radars at 79 GHz
wind turbines
important but not allocated RAS bands and new technologies
more [and younger] astronomers needed at ITU/regional levels!