## Slide 1: A reinvigorated US fusion energy program
Reflecting, in part, discussions with T. Carter, R. Fonck, M. Haynes, D. Maurer,
D. Meade,G. Navratil, G. Tynan, D. Whyte
S. Prager
Princeton University

## Slide 2: The committee charge is large and expansive
To advance the US to world leadership in fusion research
To develop fusion energy as a priority for the US
Projecting both near- and long-term
This is a crucial and timely opportunity for the US fusion research
(and for the field of plasma physics)

## Slide 3: Fusion research at mid-life identity crisis
Several paradoxes
Technical
Timeline
US standing

## Slide 4: Technical paradox
Remarkable progress
Tokamak performance, fusion plasma physics, fusion engineering
Constructing ITER - a reactor-scale, burning plasma experiment
But,
More scientific and engineering challenges lie ahead,
Challenges of steady-state, disruptions, high performance are persistent
ITER embodies the strengths and challenges of tokamak confinement (Q = 10, but for 8 minutes),
EU DEMO embodies current knowledge base -> large, pulsed

## Slide 5: Timescale paradox
Now there is a societal desire to achieve fusion urgently
But,
The time to fusion power is paced by facility construction times (fusion cannot be proven/developed at small scale, then scaled up)

## Slide 6: US leadership paradox
The US workforce is at the world forefront (although narrowing)
But,
The US research program is not
(more later)

## Slide 7: A redefined US program can alleviate all 3 paradoxes by
Resolving technical hurdles, emphasizing innovation for improvements
Accelerating the time to fusion landmarks and fusion power
Bringing the US to the world forefront

## Slide 8: The interim charge – assess current status of US research– is substantive and important
Substantive: Deserves a frank and accurate assessment of the health and stature of the US program
Important: Defines the landscape from which a new strategic plan will be launched
Not been previously articulated “officially”

## Slide 9
Built upon major investments in 1980 – 2000
(TFTR, DIII-D, NSTX, CMOD, coupled to strong base program)
One metric is the US share of international research prizes
Nuclear Fusion prize – 8 out of 11 to work led by US scientists
Alfven Prize, EPS – US scientists won 8 out of 17 years, mainly for fusion research
US has been a world leader in nearly all areas of fusion research
This metric is a lagging indicator of investments built up over decades

## Slide 10: US is losing research leadership and vitality for 2 coupled reasons
No current strategic plan for fusion energy
absence of DOE-sanctioned community process,
no consideration of slip in ITER timeline (20 yrs to DT operations)
Lack of major investment in new US research facilities and capabilities
20 year gap in major investments (~$ 1B) in US facilities,
recent closure of CMOD (2016), closure of TFTR (1997) leaves only DIII-D (1986) and NSTX-U (1999/2019)
This contrasts sharply with our international partners

## Slide 11: Our ITER partners have roadmaps to DEMO
European roadmap

## Slide 12
EU roadmap in a nutshell
And similarly for China, S. Korea, Japan
(the US is distinct in its absence of a fusion roadmap)……

## Slide 13: Scientific facilities are increasing across the world
Korea: superconducting tokamak (2008)
China: superconducting tokamak (2006)
Japan: superconducting tokamak (2019)
New major facilities
In Asia

## Slide 14
Germany: superconducting stellarator (2016)
France: ITER
The world has entered the era of superconducting facilities (steady-state)
France: SC tokamak (2016)
In the European Union
A leading indicator
Scientific facilities are increasing across the world

## Slide 15
Collaboration on facilities abroad
An important, valuable opportunity for the US (and host labs)
But, international collaboration is not a substitute for US leadership.

## Slide 16: All fusion research sectors not sufficiently healthy
Universities:
A critical situation. Prospects for faculty positions weak, despite scientific interest. Due to decline in research projects and gov’t long-term commitment. (see UFA report, D. Mauer talk)
National labs:
Similar causes led to few national labs with MFE as priority
Industry:
Little involvement in DOE program (except GA), but new phenomenon of fusion startup companies

## Slide 17: But the stage is set for the US to transition to a dynamic, leading fusion program
We have a world-leading workforce
With many innovative and important ideas ready to pursue

## Slide 18: A new fusion strategy
Vision:
Employ new scientific advances for an improved fusion power system and an accelerated path to fusion energy,
building upon the existing knowledge base and international activities

## Slide 19: A new fusion strategy
Vision:
Employ new scientific advances for an improved fusion power system and an accelerated path to fusion energy,
building upon the existing knowledge base and international activities
Note: the following strategy is described programmatically; the underlying fundamental science is implicit, but not articulated

## Slide 20: Three premises for strategy
Pursue ideas to improve the fusion vision and accelerate its pace
New opportunities have emerged within physics and engineering for improvements and solutions to remaining challenges,
Allow for higher risk tolerance
Builds on and leverages the US and world tokamak/ITER program
Accommodates tension between staying with proven performance vs
exploring new ideas
3. Incorporates a US DT program (and facility) as an integrating goal
With a mission that complements ITER, and includes advances
since the ITER design and those that accrue through #1

## Slide 21: Features of above strategy
A distinct US approach that complements, and benefits from, the world program; departs from the dominant ITER -> DEMO -> Reactor framework (both too risky and leads to too large a reactor)
Requires a substantially restructured, reinvigorated, US program
Would restore the US to a world leadership position in fusion

## Slide 22: Examples of major new research elements suitable to a new strategy

## Slide 23: Program mission elements
Create fusion plasma core
high gain, steady-state, disruption-free, compact
Tame the plasma-wall Interface
survivable materials, plasma control
3. Harness fusion power
tritium breeding, structural materials, energy
conversion, environmental attractiveness
Establish an integrated fusion power concept that is
commercially attractive
economic, reliable, high availability

## Slide 24: In each area,
There are “big ideas,” many pioneered in the US, not being explored significantly, that can have large impact
Most ideas have “moderate cost” next steps and “substantial cost” integrating/demonstration steps;
the strategy is relatively robust to funding level
Many ideas, no one “silver bullet” for fusion

## Slide 25: Create the fusion plasma core
Realize a smaller, steady-state tokamak vision
High temperature/high field SC magnets
Low aspect ratio tokamak
Improved operating regimes
2. Develop new 3D magnetic configurations for intrinsic steady-state
Optimize stellarator for high performance
Aim toward DT facility
3. Establish a program for high risk, high payoff exploratory concepts
With an evaluation structure with metrics

## Slide 26: Create the fusion plasma core
Realize a smaller, steady-state tokamak vision
High temperature SC magnets
Low aspect ratio tokamak
Improved operating regimes
2. Develop new 3D magnetic configurations for intrinsic steady-state
Optimize stellarator for high performance
Aim toward DT facility
3. Establish a program for high risk, high payoff exploratory concepts
With an evaluation structure with metrics
A new activity,
potentially transformative

## Slide 27
β2B4 where β = p/B2
Increase B by pushing technology
(e.g, high Tc superconductors)
Increase β,κ by
pushing physics
(spherical tokamak)
~
(κβNB)4 for fixed bootstrap fraction
(βN = β/(I/aB) ,κ = elongation )
~
fusion power (pressure)2
~
Pushing fusion to smaller size

## Slide 28
“Compact” fusion pilot plant/FNSF
Generates net electricity,
breeds tritium, high neutron fluence
Volume within cryostat about 1/3 that of ITER
ARC design (MIT)
Major radius = 3 m
High Tc SC for high field
and/or smaller magnets
ST design (PPPL)

## Slide 29: Advancing the High Magnetic Field Approach
High Tc magnet R/D for fusion (3 – 5 years)
Prototype coil tests (incl. for 3D systems)
Develop demountable joints
(Moderate cost)
Enables a compact confinement experiment
e.g., divertor test tokamak, DT experiment
(Substantial cost)

## Slide 30: Create the fusion plasma core
Realize a smaller, steady-state tokamak vision
High temperature/high field SC magnets
Low aspect ratio tokamak
Improved operating regimes
2. Develop new 3D magnetic configurations for intrinsic steady-state
Optimize stellarator for high performance
Aim toward DT facility
3. Establish a program for high risk, high payoff exploratory concepts
With an evaluation structure with metrics

## Slide 31
Super-optimizing plasma confinement (stellarators)
3D magnetic field: no symmetry
huge magnetic design space
Merges most advanced physics and computation
W7-X
Can vary: symmetries (helical, toroidal), no symmetry, magnetic shear, curvature, aspect ratio
Optimizes: thermal confinement, energetic particle confinement, MHD stability, turbulent transport…....
Result: Steady-state, disruption-free Challenges:
Well-confined Experimental validation
High fusion energy gain Find optimum

## Slide 32: Advancing the stellarator
Begin a national optimization/design study now
Focused on design that complements international effort
(e.g., quasisymmetry, incorporate new ideas such as turbulent transport optimization, magnet simplification, energetic particle
confinement, strong flow…..)
Construct a mid-scale facility to test these ideas
  ~ moderate cost
• Advance toward a world-leadership-scale experiment
design could be similar or complementary to mid-scale facility,
(substantial cost)
All new and potentially transformative

## Slide 33
Develop liquid metal boundaries
Explore and deploy new advanced magnetic divertor topologies
Linear test stands – materials exposed to plasma flux
Explore additive manufacturing for advanced solid walls
2. Tame the plasma-wall interface

## Slide 34
Develop liquid metal boundaries
New and potentially transformative
Explore and deploy new advanced magnetic divertor topologies
Existing program, but many additional opportunities
Linear test stands – materials exposed to plasma flux
New program, moving beyond existing facilities
Explore additive manufacturing for advanced solid walls
    Largely unexplored for fusion
2. Tame the plasma-wall interface

## Slide 35
Self-regenerating,
No erosion, neutron damage, heat overload (if moving)
Highly absorbing (if lithium): no influx to plasma, improves confinement,
Many science and engineering challenges to establish feasibility
Liquid metals for the plasma-facing material

## Slide 36: Developing Liquid Metal Boundaries
• Broad R&D program: next 5 – 7 years
Surface science studies
Linear test stands
Liquid flow tests
Studies in existing toroidal facilities
(Moderate cost)
• Integrated fusion facility with LM boundary
Integrated viability of liquid surfaces,
Engineering design/construction begin in ~ 5 years,
Possibly two stages – divertor, full wall
(Substantial cost)

## Slide 37: 3. Harness fusion power
Materials and blanket research
  compact neutron source
  innovative blankets (immersion, DCLL)
  (moderate cost)
US DT facility: Initiate now a community planning process for possible missions, complementing ITER:
Fusion nuclear science facility (FNSF)
High gain burning plasma science (Q > 10)
Pilot plant (net electricity)
(very substantial cost)

## Slide 38: US DT Facility
Next 3-5 years:
Identify mission
(FNSF, high gain burning plasma science, net electricity)
Develop optimal path(s) to a DT experimental program
(e.g., AT, ST, high field, optimized stellarator…...)
In 3-5 years:
Review status and decide mission/timing of DT facility

## Slide 39: Increasing opportunities in computation and theory
Computation (at all scales, up to exascale), in concert with theory, underlies all fusion topics
Tremendous opportunities are strongly in line with DOE/national emphasis on large-scale computation

## Slide 40: With or Without the US in ITER
Above strategic vision and goals are unchanged ⇒ the strategy is relatively robust
If US not in ITER: affects timing and mission of US DT program, decreases emphasis on ITER prep research
Although if the US pulls out, an earthquake could result with unpredictable consequences

## Slide 41: This strategy would be a 4th shift for fusion research
70s/80s: Surge in tokamak research (facilities)
Tokamak performance/understanding exploded
mid-90s: Restructuring: shift to science foundations CIT/BPX TFTR TPX & US out of ITER,
Succeeded in reinvigorating fusion science
mid-2000s: Presidential ITER initiative and coordinated world effort
ITER moves forward as focus of world program
but, US domestic capabilities wane relative to world
2018: Establish an aggressive program, exploiting new innovative ideas, to carry the US to fusion energy:
Re-assert US leadership

## Slide 42: Typical fusion plan in other nations (simplified)
ITER
High performance,
steady state
Plasma-material
interface
Solid tungsten (tokamaks and test facilities)
burning
plasmas
Tokamaks, limited stellarator
Fusion nuclear science
Integration
Large-tokamak DEMO
Blanket development studies, TBM in ITER, possible IFMIF

## Slide 43: A sample new US program in the international context
ITER
High performance,
steady state
Plasma-material
interface
Solid tungsten (tokamaks and test facilities)
burning
plasmas
Tokamaks, limited stellarator
Fusion nuclear science
Integration
Large-tokamak DEMO
Blanket development studies, TBM in ITER, possible IFMIF
Liquid metals (tokamak, test facilities)
An HTS reduced size tokamak/ST; a unique-design stellarator
Reduced-cost BPX, FNSF, or Pilot Plant
Compact neutron source, innovative blanket designs
More compact DEMO

## Slide 44: The above can be described via challenges in fundamental science
A burning plasma is itself a major physics accomplishment – a new complex, physical system
The strategy is driven by major questions in
plasma physics (turbulence, self-organization, breaking of magnetic topology, symmetry effects…..),
material science (under extreme conditions)
The connections to other areas of science is large and specific
(astrophysics, complex systems, accelerator physics.....)

## Slide 45: How should fusion R/D be organized within DOE?
The Office of Science (FES) must remain a key sponsor, given the remaining fundamental challenges in plasma physics and material sciences
The Office of Science cannot tackle all the critical challenges in fusion engineering and technology
Thus, a possible approach is to sponsor fusion energy research in both OS and an applied energy office, coordinated from above

## Slide 46: Closing comments
A frank assessment of the health of the current program is important, and sets the stage from which to grow a new strategy
A new strategy emphasizing innovations for an improved fusion system concept and accelerated path
Can be embarked upon with moderate new funds,
Forms the basis for aggressive roadmap to fusion power,
Builds constructively upon the current program,
Re-establishes the US as a world leader,
Is scientifically exciting