## Slide 1
Perspective on Fusion Energy Strategy
By
Tony S. Taylor
With
M. Wade
W. Solomon
Presented at
NAS Committee for a
Strategic Plan for U.S.
Burning Plasma Research
August 29, 2017

## Slide 2: Fusion Energy is at a Crossroads in the U.S.
ITER construction underway
  Exciting and vital validation of the fusion energy concept
World program considering major facilities beyond ITER
Japan DEMO
EU DEMO
Central Solenoid
K-DEMO
CFETR
World program is moving ahead aggressively with fusion energy development. What path with the U.S. take?
ITER

## Slide 3: Your Charge to Me
We would especially appreciate learning your views on:
The importance of U.S. burning plasma research to the development of fusion energy,
The scientific and technical developments since the 2004 report of the NAS Burning Plasma Assessment Committee
The current status of U.S. research that supports burning plasma science including U.S. scientific support for ITER
Any strategic elements that might strengthen or accelerate U.S. burning plasma research given that economical fusion energy within the next several decades is a U.S. strategic interest.

## Slide 4: Importance of Burning Plasmas
Executive Summary:
Burning plasmas are a critical next step towards the realization of fusion energy
Tokamak physics is sufficiently advanced to support burning plasma step, and the tokamak remains the only fusion concept mature enough to proceed to the burning plasma step
Strongly recommend that this committee reaffirm the importance of burning plasmas in fusion energy development, the highly developed status of tokamak plasma science, and the unique opportunity that ITER provides the U.S.

## Slide 5: Burning Plasma: First Major Step on Path to Fusion Energy Other Steps: Build on a Burning Plasma to Complete
Scientific
Basis
Fusion Energy
Deployment
For DEMO, technical readiness must be established for:
  Fusion power source
  Materials
  Breeding Tritium & Extracting Heat
Successful burning plasma experiment facilitates progress in materials and blanket technology
Foundational Science & Technology
Burning Plasmas
Materials
Tritium Breeding
Heat Extraction
Integrated
Demonstration
Notes: Have to say that fusion energy development requires the burning plasma step.
A key question is how important is the burning plasma step without the energy goal?
All panels that have addressed Burning Plasmas have affirmed the importance of burning plasmas - and affirmed BP as the next critical step on the path to fusion energy
FESAC 1996
Snowmass
FESAC 2003
NRC 2004
NAS 2010

## Slide 6: A Burning Plasma Will Enable Frontier Fusion Science
Self-sustained fusion plasma is a highly nonlinear system
  Self-generated heating & magnetic fields  complex behavior
  “Grand Challenge” for theory and numerical modeling
A burning plasma experiment and the supporting scientific program will advance basic plasma science
  Plasma turbulence, magnetic field line reconnection, wave-particle interactions, …
  Applicable in other regimes (e.g. astrophysical plasmas)
“A burning plasma experiment can offer substantive and important contributions to other fields of science connected to plasma physics, primarily through experimental access to the fundamental and/or extreme conditions offered by such a state.”
– Burning Plasma, NRC Report

## Slide 7: Burning Plasmas are both a Challenge and an Enormous Scientific Opportunity
Challenge: Produce burning plasma conditions and then maintain them
  Achieve necessary density/ temperature/confinement (n T t)
  Operate safely at high plasma pressure
  Handle concomitant heat/particle flux
  Minimize/Eliminate effect of transients
Opportunities enabled:
  Alpha-particle impact on stability & turbulence
  Turbulent transport and resistive MHD at low r* (relative gyroradius) and rotation
  Fusion burn stability, control, and propagation
  Strong, non-linear coupling of heating, current drive, turbulent transport, MHD stability and boundary plasma
ITER
C-Mod
Realization
Exploitation
NSTX
DIII-D
JET
MAST
ASDEX-U
SST-1
EAST
KSTAR
JT-60SA
TCV
Physics Basis

## Slide 8: A Burning Plasma Experiment Drives Advances in Fusion Technologies
  Large, high field magnets
  superconducting if long pulse
Remote maintenance and handling
  Tritium processing systems
  Hardened diagnostics
  High heat flux energy removal systems
  Long pulse, high power density heating and current drive systems
  Plasma current quench detection/remediation systems
  Integrated control systems for the nuclear plant and plasma, including burn control
  Desired: test blankets for tritium breeding
  …

## Slide 9
Tokamaks Presently at Highest Level of Readiness of Any Concept to Exploit Burning Plasmas
ITER
Stellarator ~2020
Achieved tokamak performance is two orders of magnitude above other concepts
Physics basis is well established (ITER Physics Basis in NF 1999, 2007)
  Recent advances in later section
Strong Worldwide Research Program
  Complementary and versatile facilities
  Well diagnosed  solid science
  Theory & simulation  prediction
  Advanced plasma control
  Large, capable work force
  Tokamak is well positioned for continued scientific advances and innovation
Notes: Reference for W7-X
Plasma phys. Control. Fusion 58 (2016) 074006

## Slide 10: Previous Panels Have Affirmed the Importance of Burning Plasmas and Opportunity to Participate in ITER
NRC Burning Plasma Report 2004
“Participation in a burning plasma experiment is a critical missing element in the U.S. fusion science program”.
“The United States should participate in the International Thermonuclear Experimental Reactor (ITER) project”
“Progress toward the fusion energy goal requires this step”
“There is now high confidence in the readiness to proceed to the burning plasma step.”
“The tokamak is the only fusion configuration ready for implementing such an experiment.”
NAS Decadal Study 2010
“It is clear that the next critical step in the development of fusion power is a burning plasma experiment. ITER is that step.”
Strongly recommend that this NAS committee reaffirm the importance of burning plasmas and the unique opportunity of ITER

## Slide 11: Scientific Developments since 2004 NAS Report
Executive Summary:
The understanding of key physics governing underlying performance has advanced dramatically
The U.S. fusion program remains at the forefront of fusion science.
Research since the NAS Burning Plasma Report (2004) has strengthened our confidence in burning plasma (ITER) performance.

## Slide 12: Scenarios Match ITER Q=10 Dimensionless Parameters Relevant to Fusion Power & Gain in Present-Day Expts
Issue | ITER Physics Basis (1998, 2007) | Present
Rotation | Co-NBI, high rotation | Zero applied torque solutions found
Electron heating | Ion dominant | Electron dominant heating explored
Operational issues | Basic EC/low voltage startup, rampdown in constant shape | Integrated tests of EC startup and rampdown with shape control
ELM mitigation | First indications of mitigation by RMP | RMP ELM suppression in baseline and advanced scenario, pellet pacing
Heat flux mitigation | Basic radiative divertor demonstration | Radiative divertor in operating scenario
Disruption mitigation | Basic physics understood | MGI and SPI tested
PMI | Mostly in graphite walls | Direct tests of ITER-like wall
ITER baseline
Advanced

## Slide 13: Theory-Experiment Validation Has Increased Confidence in ITER Achieving its Q=10 mission
2004 status:
Manually-intensive “Herculean” simulations. Missing first principle pedestal model, rotation etc
2017 status:
Self-consistent coupling of core & pedestal theoretical models
Enables prediction and optimization of ITER fusion gain: Q~12 possible
(TGLF+NEO)
Romanelli Plasma Fus. Res 2014
Meneghini Nucl. Fusion 2017,
Snyder Nucl. Fusion Award 2014
Profile Prediction (OMFIT, IPS, TRANSP, TGYRO using TGLF, NEO, EPED)
Notes: Orso says that they only do flux matching using TGLF+NEO between 0.3<rho<0.8 using TGYRO as indicated on the figure. He does this to avoid the drift-ordering break down near the axis and to avoid dealing with sawteeth. instead he has an approach to use a linear profile of inverse gradient scale length from the magnetic axis to rho=0.3.
The JINTRAC system of codes for integrated simulations couples the JETTO transport solver for the core, and EDGE2D for the edge region. It has been used in simulations to evolve a JET discharge from L-mode through the L-H transition to ELMing H-mode and a subsequent back transition to L-mode after the beams are later turned off.

## Slide 14: Major Advancement in Core Fluctuation Diagnostics Have Enabled Detailed Validation of Fast Ion Transport Models
ECH modification of RSAEs in DIII-D
fRSAE-min
fTAE
fTAE
fRSAE-min
2004 status:
Alfven Eigenmodes and associated transport observed and characterized
2017 status:
Fast-ion instability control tools show promise
First principles simulations reproduce measured modes & transport (MEGA)
Reduced predictive models based on critical gradient
Van Zeeland Nucl. Fusion 2016
Y. Todo Nucl. Fusion 2016
Sharapov IAEA 2016
Notes: More recent publications using MEGA to simulate fast ion transport, profile stiffness and flattening include:
Y Todo 2016 New Journal of Physics 18 115005
Y. Todo et al 2016 Nuclear Fusion 56 112008
New diagnostics
FIDA -- fast ion D-alph
ECEI -- electron cyclotron eimission imaging
Interferometry -- very high bandwidth Hz
Variable beam voltate --and input distribution

## Slide 15: ELM Suppression Achieved in Fully Non-Inductive Hybrid Plasma with Minimal Impact on Performance
2004 status:
Proof-of-principle demonstrations of RMP ELM suppression, pellet pacing, and QH-mode
2017 status:
Extension of all technique towards ITER conditions
Long-pulse ELM suppression
I-mode developed, QH-mode operation expanded
Role of plasma response and field penetration
Petty Nucl. Fusion 2017
Oh IAEA 2016
Sun IAEA 2016
161403
0.0
0.4
0.8
1.2
0
1
2
3
4
-0.2
0.0
0.2
0
1
2
3
IP (MA)
ECCD
NBCD
bootstrap
Vsurf
(V)
bN
qmin
IRMP (kA)
Da
0
1
2
3
4
5
6
Time (s)
4
DIII-D Hybrid scenario

## Slide 16: Major New Understanding in SOL Heat Flux Channel Width Developed Through Joint Experiments
2004 status:
Conflicting experimental data on heat flux width; large experimental uncertainties
2017 status:
ITPA empirical scaling developed setting potential challenge for 15 MA ITER discharges (lq ~ 1mm)
High performance computing enabling gyrokinetic simulations of heat flux width
New role of electron turbulence found in simulations which may significantly broaden heat flux
Goldston Nucl Fusion, 2012
Eich, Nucl. Fusion, 2013
Chang, Nucl. Fusion, 2017,

## Slide 17: Major Advances Have Been Made to Understand Tungsten Behavior Under Extreme Conditions
2004 status:
Most devices favor low-Z wall for plasma performance
2017 status:
ITER to start operation with full-W divertor
JET ITER-like-wall (ILW) used to characterize tritium retention, fuel removal, cracking, melting, dust, plasma performance
  Low T retention (0.3%)
  Similar core confinement, pedestal Te reduced
Surface modifications (He-fuzz)
Litaudon Nucl. Fusion 2017
Baldwin Nucl. Fusion 2008
ITER Divertor

## Slide 18: Powerful Tools Have Been Developed to Predict and Avoid Disruptions
Extensive suite of disruption avoidance techniques
  NTM control by ECCD, MHD instability control, MHD spectroscopy
Advanced disruption warning systems predict oncoming disruptions
  NSTX: > 96% disruptions caught, < 3% false alarm
  JET: > 98% disruptions caught, < 1% false alarm
S. Gerhardt Nucl. Fusion 2013
A. Murari, ITPA MHD (2013)

## Slide 19: Strong Progress in Explaining Fast Dissipation of ‘Runaway’ Electrons at Plasma Termination
2004 status:
Critical electric field quantified, additional terms starting to be explored
2017 status:
Simulations capture underlying dissipation mechanisms
Dominant RE seed processes discovered (hot tail)
RE control developed
Strong U.S. focus
Experiment
SciDAC SCREAM
BPO task group
ORNL/DIII-D pellets
g ray camera
Anomalously high dissipation
Shattered
pellet
DIII-D
ITER
New impurities model
Increased dissipation
Paz-Soldan PRL 2017
Hesslow PRL 2017
Notes: ANOMAOUS DISSIPATION – NOTE EXP AND THEORY ARE DIFFERENT REGIMES AND EFFECTS
Increases in critical electric field. Progress in theory and experiment in explaining anomalously fast dissipation of REs.
(Bold claim was these additional dissipation effects had not been included before - this is not as new as it was sold).
Note different regimes – no argon vs argon. Theory case is singly stripped.
Relevant to mitigation scenario – use impurities to dissipate runaways.
Closing in on agreement with theory.
Note that first experiment obserfation presented by Hollman 2013 (2012 IAEA)
SCREAM SciDAC Simulation Center for Runaway Electron Avoidance and Mitigtion.
BPO: Disruption Task Group Val Izzo, Bov Granetz

## Slide 20: Progress Since the 2004 Burning Plasma Report Has Strengthened Our Confidence in BP Performance
Topic (example) | 2004 | 2017
ITER Operational Scenarios | Isolated examples of performance, high rotation, ion heating | Integrated solutions Extended toward ITER conditions (low rotation, e-heating) JET ILW
Pedestal | Peeling-ballooning theory developed | Predictive model of pedestal performance validated against experiments
Energetic particles | AEs observed, basic mode properties and associated transport characterized | Advanced fluctuation and fast ion distribution measurements First gyro-kinetic simulations reproduce measurements Reduced predictive models based on critical gradient
Disruption mitigation and avoidance | Massive gas injection for fast shutdown, limited capabilities on disruption avoidance & mitigation characterization | SPI technique Understanding of radiation asymmetries Real-time stability calculations & disruption predictors

## Slide 21: Progress Since the 2004 Burning Plasma Report Has Strengthened Our Confidence in BP Performance
Topic (example) | 2004 | 2017
Runaway electrons | Critical electric field quantified + other terms being explored | Simulations capture underlying dissipation mechanisms RE control developed
ELM control | Proof-of-principle demonstrations of RMP ELM suppression, pellet pacing, and QH-mode | Extension towards ITER conditions Understanding of stability limits
Error Fields | Simple vacuum field understanding | Predictive models with plasma response and field penetration
Transport | Gyrokinetic codes and reduced transport models being developed | Multi-field, multi-scale simulations compared with data Improved fidelity reduced models
Integrated modeling | Manually intensive “Herculean” simulations. Missing first principle pedestal model, rotation etc | General frameworks developed for streamlined integrated workflows High fidelity models using high performance computing

## Slide 22: Progress Since the 2004 Burning Plasma Report Has Strengthened Our Confidence in BP Performance
Topic (example) | 2004 | 2017
Plasma control | Feedback control of 0D plasma parameters | Profile control Offline control developed by simulation
Divertor power handling | Demonstration of heat flux reduction in low-Z tokamaks | Extended to metal walls Feedback control of divertor heat flux
SOL heat flux width | Conflicting experimental data on heat flux width | ITPA empirical scaling developed New role of electron turbulence predicted in gyrokinetic simulations
Divertor geometry | Standard configurations with limited poloidal flux expansion | Advanced divertor configurations with increased poloidal/toroidal flux expansion
PMI | Individual research on local surface, global migration, SOL transport | Integrated studies between core/edge/wall Mixed wall and ITER-like wall material studies

## Slide 23: Status of World-Wide Research That Supports Burning Plasma Science
Executive Summary:
The world program is focused on preparing for burning plasmas in ITER
ITER has been highly effective as a forcing function for driving progress in fusion science and technology.
World tokamak program is well positioned to address any emerging issues with regard to ITER operations and successful attainment of Q=10
U.S. facilities are highly capable research platforms for innovation and understanding

## Slide 24: The World Program Is Focused on Preparing for Burning Plasmas in ITER
NSTX-U
DIII-D
JET
MAST-U
ITER
ASDEX-U
SST-1
EAST
KSTAR
JT-60SA
TCV
WEST
U.S. is a major contributor, and benefits greatly from participation

## Slide 25: The World Program Is Focused on Preparing for Burning Plasmas in ITER
NSTX-U
DIII-D
JET
MAST-U
ITER
ASDEX-U
SST-1
EAST
KSTAR
JT-60SA
TCV
WEST
U.S. is a major contributor, and benefits greatly from participation
International partners provide
Stronger scientific basis
Broad team, range of facilities, tools, and experience
Industrial fabrication capabilities
Shared costs

## Slide 26: The World Fusion Community is Organized to Carry Out Burning Plasma Research
International Tokamak Physics Activity (ITPA) makes key contributions to coordinating worldwide burning plasma research through joint experiments on multiple devices
  ~ 850 scientists from all 7 ITER parties (US, China, EU, India, Japan, Korea, Russia) plus Australia
  7 Topical Groups focus research in key areas
    Diagnostics, Divertor-Scrape-Off-Layer, Energetic Particles, Magnetohydrodynamic Instabilities, Pedestal & Edge Physics, Transport and Confinement, Integrated Operating Scenaros
  Semi-annual meetings convene 30-40 members and other experts
    State of the art burning plasma research discussed
    Multi-machine joint research proposals generated
    Recommendations for ITER generated
  Over 100 refereed journal publications produced directly from ITPA topics in last 5 years
The US plays a substantial role in ITPA experiments and documentation activities
  Over 200 US scientists

## Slide 27: ITPA Success Story: ELM Suppression by Magnetic Perturbations Verified on US and EU Tokamaks
ELM Suppression using internal coils on DIII-D initially formed the basis for adding 3D coils to the ITER design
ITPA Joint Experiment organized to reproduce ELM suppression on other tokamaks
DIII-D and ASDEX-Upgrade joint experiment led to the first observation1-3 of ELM suppression in AUG, confirming basis for ITER
R. Nazikian, W. Suttrop et al. Proc. 26th IAEA Fusion Energy Conf., Kyoto, Japan (2016), to be submitted to Nuc. Fusion
W. Suttrop, R. Nazikian et al., submitted to Phys. Rev. Lett. (Nov 2016)
W. Suttrop, R. Nazikian et al., Proc 44th European Phs. Soc. Conf., Belfast, N. Ireland (July 2017), to be submitted to Plas. Phys. Control. Fusion

## Slide 28: ITER Project is Coordinating Additional Research Activities Involving World Community
ITER Research Plan
  Developed in collaboration with community experts worldwide, this document outlines the anticipated content and schedule for research activities on ITER
ITER Integrated Modeling Expert Group
  Help guide the ITER integrated modeling program and to act as an interface between member physics modeling programs and the ITER organization.
ITER Scientist Fellow
  Prepare for the scientific exploitation phase of the device by strengthening the involvement of the fusion community directly with ITER. Interact closely with the ITER Science & Operations Department in the definition of a research program
ITER Operations Network
  Provide advice and feedback to the ITER project in the Operations area…”
Notes:   ITPA has resulted in the achievement of a broad physics basis essential for the ITER design and useful for all fusion programs and progress toward fusion energy generally
  contribute to the preparation of the documentation which will constitute the definition of the ITER operations framework

## Slide 29: Complementarity/Uniqueness of World Tokamak Facilities Continue to Advance Fusion Toward Burning Plasmas
Complementarity enables multi-platform development and evaluation of key physics
Uniqueness promotes evaluation of new ideas that emerge from synergistic collaborations across facilities
Tokamak | Key Contributions to Burning Plasma Science
DIII-D | Scenarios, transients, control, EPs
NSTX-U | Low R/a physics, EPs, transients
JET | Tritium, size scaling, ITER-like wall
AUG | Transport, divertor, tungsten wall
TCV | Shaping effects on core and divertor
MAST-U | Low R/a physics, advanced divertor
WEST | Long-pulse tungsten divertor
EAST | Long-pulse scenarios, core/edge compatibility, metal walls
KSTAR | Long-pulse physics, 3D fields, H&CD technology
JT-60SA* | H&CD technologies, advanced scenario demonstration
ITER* | Integrated burning plasma demonstration
*under construction
  Well positioned to advance burning plasma science in preparation for and in concert with ITER

## Slide 30: U.S. Facilities: Excellent, Cost-Effecve Research Tools to Provide World-Leading Fusion Science
DIII-D and NSTX-U provide world-leading and complementary capabilities to resolve scientific Issues for fusion energy
  Mature facilities with established infrastructure and experienced staff
  Highly flexible, 2D shaping, controlled 3D magnetic perturbations,
  Well diagnosed: in-depth scientific investigations and model validation
  Divertor structures top and bottom, easily modified
  National and international research teams
  Low vs high torque and ρe
  Complementary current drive (ECCD, Helicon vs HHFW, helicity injection)
  Complementary boundary approach (cryopump vs lithium, solid vs liquid)
DIII-D
NSTX-U
  Train the next generation of scientists and engineers
Notes: U.S. Facilities : Excellent Research Tools to provide frontier (cutting-edge) (world-leading) fusion science
Mature facilities with established infrastructure, experienced operations staff -> safe reliable operattion
World leading and complementary capabilities
Comprehensive set of diagnostics enables in-depth scientific investigations and model validation
Powerful set of control tools
H & CD, flexible shaping , density control with cryopumps, flexible 3d coil set
Divertor structures top & bottom, easily modified.
International Team

## Slide 31: US Theory and SciDAC Burning-Plasma Research: Rapid World-Leading Advances in Predictive Capability
  Develop and support world-class numerical tools
  GYRO, GS2, GTC, GEM: electromag. turbulence
  M3D-C1, NIMROD; nonlinear extended MHD
  BOUT, ELITE, XGC1, COGENT, UEDGE: bound. & PMI
  TGLF, NEO, EPED: core/pedestal prediction
  OMFIT, TRANSP, ISP: integrated simulation
  AORSA, NuBEAM, CQL3D: RF sources
  Address important burning plasma issues
  Performance prediction with coupled core & pedestal  higher confidence, optimization
  Pedestal transport and L-H transiton
  Plasma response to 3D fields ELM suppression
  Simulation of RE dynamics and disruption mitigation scenarios
  Critical gradient and resonance broadening EP transport models
  Strong U.S. partnership between theory & experiment
  Model validation
  Interpret, direct, and predict experiment discovery and innovation in fusion research
Multi-Scale Turbulence (GYRO)
EPED Super H-Mode Prediction
Theory  experiment
electron scale
ion scale
GYRO dTe/Te0

## Slide 32: U.S. Leadership In Burning Plasma Research Evidenced By Nuclear Fusion Prize Recipients (won 8 of 11)
Luce, Scenarios, 2006
Evans, ELM Suppression, 2008
Rice, Intrinsic Rotation, 2010
Sabbagh, Stability, 2009
Diamond, Rotation Theory, 2012
Whyte, Scenarios, 2013
Goldston, SOL physics, 2015
Snyder, Pedestal, 2014

## Slide 33
Executive Summary:
Realizing fusion energy within the next several decades will require increased funding and reduced costs.
ITER provides the most timely and capable option for the U.S to exploit burning plasmas.
The U.S. should develop a strategic plan with exciting stage milestones targeting a U.S. cost-attractive DEMO in the next several decades
Fusion energy development requires an increasing effort in fusion materials and fusion nuclear science
Strategic Elements to Strengthen or
Accelerate U.S. Burning Plasma Research
Strategic elements in mostly considering the United states is a partner in ITER

## Slide 34: Electricity Demand in Next 100 Years Presents Major Challenges and Also Tremendous Opportunity
Projected need for ~ 35,000 GW from non-CO2 producing sources
35,000 1 GW-e plants !!!
Consequently, annual investment in energy projected to explode
  $0.8T by 2050
  $2.5T by 2100
   Timely positioning is key
*Message AMPERE2-450-FullTech-OPT Scenario
Integrated emissions limited to maintain CO2 levels below 450 ppm , full technology
Strategic Interest for the U.S. and the World

## Slide 35: Substantive Progress Towards Fusion Energy Requires a) Increased Funding and/or b) Reduced Costs
Koepke, 2014
  International partners are needed to develop fusion energy

## Slide 36: What is Required to Increase Funding
Provide an exciting vision for the future to motivate increased public and political support, funding and attract the brightest and best researchers
Work to unify the community, get the community working together
  Requires community leadership and engagement, perhaps a process similar to that of 1998 - 2004
Establish a partnership between the Feds (OFES, OS) and the community
Resolve to maintain a strong U.S. commitment to the path forward
Engage the entire U.S. fusion community in burning plasma research: planning, preparing, and execution.
  Community must own the path forward as their path forward
  Required to maintain community unity and commitment
Recommendation: FES and the U.S fusion community should begin a process to develop a roadmap and strategic plan

## Slide 37: Accelerating the Path to Burning Plasmas and Fusion Energy Development
Ages-old quip: “Fusion is 50 years away and always will be.”
How to reconcile?
NAS charge: “given that economical fusion energy within the next several decades is a U.S. strategic interest”

## Slide 38: Accelerating the Path to Burning Plasmas and Fusion Energy Development
The Challenge
  Very challenging problem  Robust funding required
  Multiple challenges must be resolved Strategic plan required
  Staging of elements essential  Community consensus needed
Ages-old quip: “Fusion is 50 years away and always will be.”
How to reconcile?
NAS charge: “given that economical fusion energy within the next several decades is a U.S. strategic interest”

## Slide 39: Accelerating the Path to Burning Plasmas and Fusion Energy Development
The Challenge
  Very challenging problem  Robust funding required
  Multiple challenges must be resolved Strategic plan required
  Staging of elements essential  Community consensus needed
Ages-old quip: “Fusion is 50 years away and always will be.”
How to reconcile?
NAS charge: “given that economical fusion energy within the next several decades is a U.S. strategic interest”
The Solution
  Compelling vision for energy mission  Increase available funding
  Vetted strategic plan  Inform prioritization of available funding
  Broad community consensus  Unified purpose and messaging
  Bold leadership  Implement & execute difficult priority choices
    --- All done in partnership with Office of Science and FES ---

## Slide 40: Accelerating the Path to Burning Plasmas and Fusion Energy Development
The Challenge
  Very challenging problem  Robust funding required
  Multiple challenges must be resolved Strategic plan required
  Staging of elements essential  Community consensus needed
Ages-old quip: “Fusion is 50 years away and always will be.”
How to reconcile?
NAS charge: “given that economical fusion energy within the next several decades is a U.S. strategic interest”
The Solution
  Compelling program vision  Increase available funding
  Well informed strategic plan  Inform prioritization of available funding
  Broad community consensus  Unified purpose and messaging
    --- All done in partnership with Office of Science and FES ---
My recommendation:
Fully participate in ITER as the U.S. Burning Plasma Experiment
Develop a strategic plan with exciting staged milestones targeting a U.S. cost-attractive DEMO in the next several decades

## Slide 41: U.S. Should Fully Participate in ITER as the Most Direct and Fastest Path to a Burning Plasma
Observations
All fusion programs worldwide have chosen ITER as the most expedient means to burning plasmas on their path to fusion energy development
  Broad consensus on goals, responsibilities, and ownership
  Broad worldwide participation in burning plasma research
The framework for pursuing a project of this magnitude is now in place with established design and construction teams, infrastructure, nuclear license…
  Established mechanisms for timely resolution of emerging issues
ITER construction is progressing rapidly under new management
  Clear communication, responsibility, and accountability structure
Planning and preparation for operations and exploitation are beginning
Recommendation: Fully fund U.S. contributions to ITER
  Guarantee on-time, on-spec delivery of U.S. in-kind contributions
  Enable ITER IO to address emerging issues in timely, efficient manner
  Expand breadth of U.S. community efforts in burning plasma research
  These efforts/activities take time and money

## Slide 42: Strategic Plan Assertions and Principles
Assertions
Burning plasma R&D is the next major step for fusion development
ITER represents the most timely, capable option for a U.S. burning plasma experiment
Materials and nuclear science challenge is formidable and early resolution of key challenges is critical for timely delivery of fusion energy
Tokamak is the most expedient path to fusion energy
Principles
Enable development of attractive fusion energy as soon as possible
Timeliness over attractiveness of end product (power plant)
Build on existing strengths
Maintain high level of scientific excellence
Value innovation
Leverage capabilities of international partners

## Slide 43: Realization of Attractive DEMO Will Require Closing the Feasibility Gap in Three Areas Required for Fusion Energy*
Fusion Power Source (Neutrons)
Materials for Fusion Environment
Harnessing Fusion Power
Approximate Technical Readiness Level
DEMO
* Priorities, Gaps, Opportunities … 2004
A successful burning plasma experiment will leave significant gaps in fusion materials and blankets

## Slide 44: Developing Key Elements of a Strategic Plan
Support a significant community effort to provide a more in-depth evaluation of opportunities for a more cost attractive DEMO or power plant. (systems studies)
  Define domestic R&D needed to validate opportunities
Support a community/FES process (follow-on to present community workshops) to develop a long term fusion strategy/roadmap targeting a U.S. cost-attractive DEMO in the next several decades.
  Include exciting staged milestones
Strategy should include
  Robust support for engaging in burning plasma physics
  Plans for solid foundational physics; engaging universities, industry, and national labs
  A strong theory and computation program
  Plans for new U.S. fusion facilities
  Plan (how/when) to transition from existing facilities to new facilities
  A growing effort in fusion material development and testing
  A growing effort in developing fusion blanket research
  Challenge: broad effort is needed, requiring significant funding
  Difficult priority choices are required

## Slide 45: The U.S. Strategic Plan Must Include a Robust Tokamak Effort
To support and prepare for burning plasma research (ITER)  exploitation
To prepare for a cost effective DEMO
To train fusion scientists and engineers for the future
Key elements of a tokamak program should include
Plasma exhaust (divertor, materials)
Disruption prediction and avoidance
Steady-state
Predictive capability
Optimize performance (nTτ/RB)
  Proposals for cost effective Demos include significantly improved confinement (~ 1.6 - 1.8) and stability.
Enabling Technologies
  Magnet Development program -> demonstrate large, high field magnet with high temperature superconductors
  Current drive?
  Facility: new tokamak facility or upgrade of existing facility
Notes: H89P for ARIES II is 2.65 ~1.6 H98y
ARC (B.N Sorbom, Aug 2015) H89p =2.8 is ~ H98y = 1.8
If ITER assumed H98Y of 1.8, then R*B could be 1.8 smaller - 3.5 m
1.6 3.9m

## Slide 46: A Growing Effort in Fusion Materials and Fusion Nuclear Science is Required to Advance Fusion Energy
  Materials
  Develop new materials (BES: materials by design); plasma facing, structural
  Test materials in a plasma environment
    Linear devices, such as MPEX
    Fusion facility environment (tokamak, …) effect of material response on plasma performance is critically important
  Test material in high energy neutron environment
    Gap in the world program
    Potential opportunity for cost effective volume neutron source (Gas dynamic Trap), or integrated nuclear science test facility (FNSF)
Fusion Blankets
  Propose next step is a multi-effect, non-nuclear blanket test facility
  Develop a long term strategy and plan for U.S. fusion blanket development, in the context of the international program.
We will require a growing workforce of scientists and engineers with expertise in materials and fusion nuclear science

## Slide 47: Summary
Reaffirm previous panel reports stressing the importance of burning plasmas
Burning plasmas are the next step in fusion energy development
Recommended Actions:
ITER represents a unique opportunity for the U.S. to pursue burning plasmas
Capitalize on the substantial human, technical and fiscal investment made in ITER
Feasibility gaps in materials and blanket technology offer rich scientific opportunities
Develop a strategic plan with exciting staged milestones leading to a cost-attractive DEMO