## Slide 1
ITER
The way to a new, clean, safe and nearly-unlimited energy
Bernard BIGOT, Director-General, ITER Organization

## Slide 2: Fusion on Earth
A plasma of Deuterium + Tritium (hydrogen isotopes) is heated to more than 150 million °C.
The hot plasma is shaped and confined by strong magnetic fields.
Helium nuclei sustain burning plasma.
Neutrons transfer their energy to the Blanket .
In a fusion power plant, conventional steam generator, turbine and alternator will transform the heat into electricity.
τ
1 gram of fusion fuels = 8 tons of oil
0.7 MeV
Notes: Keep hot plasma KD: “will” transform
Hot to High energy,
alpha particles

## Slide 3
A new energy source of massive, predictable and potentially continuous or variable power complementary of the renewable energies
Safe, environmentally responsible
Almost limitless supply of fuel for hundreds of millions of years, widely distributed around the globe
No CO2 or other greenhouse gases
No long-lasting high-activity radioactive waste
Fusion’s advantages
A plasma in the European tokamak JET

## Slide 4
60 years of constant progress
TA-2000,
France, 1957
DIII-D, US
- 1978
General Atomics - DOE.
KSTAR, Korea
2008
WEST, CEA-Euratom, 1988, now testbed for ITER

## Slide 5
DT Fusion demonstrated!
Among the large tokamaks that went into operation in early 1980s, two were designed to perform Deuterium-Tritium operations: the European JET and the American TFTR. Both achieved DT fusion : JET in 1991 (2 MW of fusion power) and 1997 (16 MW); TFTR in 1993 (6.2 MW) and 1994 (10 MW). However, both machines had required more energy to « light the fire » than the fire had given in return (ratio of Q ~ .65). ITER aims for a ratio of Q > 10.

## Slide 6
A decisive political push
November 1985
At the Geneva Summit Presiden Reagan and Secretary General Gorbatchev give a decisive political push to an international collaboration on fusion “for the benefit of all mankind”…

## Slide 7
To demonstrate the scientific and technological feasibility of fusion power for peaceful purposes
ITER is the only magnetic fusion device under construction aimed to produce a burning plasma.
Input (heating power): 50 MW
Output (fusion power): 500 MW
ITER mission

## Slide 8
A multinational scientific collaboration without equivalent in history
A large-scale experiment to demonstrate the feasibility
of fusion energy
ITER

## Slide 9
The seven ITER Members represent more than 50% of the world’s population and about 85% of the global GDP
China EU India Japan Korea Russia USA
28 June 2005: The ITER Members unanimously agreed to build ITER on the site proposed by Europe
21 November 2006: The ITER Agreement was signed at the Élysée Palace, in Paris.
Global challenge,
global response
Notes: KD: “represent” KD: Remove “on” from dates

## Slide 10
The ITER Tokamak
R=6.2 m, a=2.0 m, Ip=15 MA, BT=5.3 T, 23,000 tonnes
Vacuum Vessel: ~ 8 000 t.
TF Coils: ~ 18 x 360 t.
Central solenoid: ~ 1 000 t.
Etc.
Total ~ 23 000 t.
3,5 times the weight of the Eiffel Tower!

## Slide 11
An intense magnetic field, generated by powerful superconducting magnets shape and confine the hot plasma, and keep it away from the vacuum vessel wall.
1 central solenoid, 13 m high, 1,000 tons, powerful enough to lift an aircraft-carrier out of the water
18 Toroidal Field Coils, 17-metre high, 360 tons each.
6 Poloidal Field Coils, 8 to 24 m. in diametre, 200 to 400 tons.
A large magnetic cage

## Slide 12
ITER Project
IO
EU
KO
JA
IN
The 7 ITER Members make cash and in-kind contributions (90%) to the ITER Project. They have established Domestic Agencies to handle the contracts to industry.
The ITER Organization Central Team manages the ITER Project in close collaboration with the 7 Domestic Agencies.
The ITER Members share all intellectual Property generated by the Project.
US
An integrated project:
Central Team & Seven Domestic Agencies
CN
RF

## Slide 13
ITER is being built through the in-kind contributions
of the seven Members of the ITER Organization.
A unique formula
China, India, Japan, Korea, Russia and the United States each have responsibility for ~ 9% of procurement packages.
Europe’s share, as Host Member, is ~ 45% (construction and manufacturing).

## Slide 14
Naval construction-size components…
Inside the Assembly Hall, giant tools (procured by Korea) will handle loads up to 1,500 tons

## Slide 15
…watch-like precision
Laser measurements of grooves in TF Coil radial plates. Tolerances are in the 1/10th millimetre range.

## Slide 16
BLANKET MODULES
DIVERTOR
MANIFOLD
INTERFACES
INTERNAL COILS
The integration challenge

## Slide 17
Conductor
China
South Korea
Japan
Russia
United States
Europe
TF Coil
Japan
TF coil cases
Japan
Europe
Managing collaboration
(The TF Coils example)

## Slide 18
Action Plan 2015
Set clear priorities and timeline for reform
Reorganized, integrated ITER Central Team with Domestic Agencies
  Clear decision processes and accountability
  Executive Project Board, Reserve Fund, Project Teams
Finalized and stabilized ITER critical component design
Comprehensive integrated bottom-up review of all activities, processes and systems
  Developed an optimized resource-loaded schedule for timely, cost-effective construction and operation through D-T plasma. Updated the 2010 Baseline.
Developed and promoted a strong, organization-wide nuclear project culture
2015: managing the need for change

## Slide 19: April 2016: intensive, in-depth review by independent expert group declares:
“…substantial improvement in project performance…”
“…high degree of motivation…
“…considerable progress during the past 12 months…”
“…sequence and duration of future activities have been fully and logically mapped in the resource-loaded schedule…”
“…resource estimate is generally complete […] and provides a credible estimate of cost and human resources…”

## Slide 20
ITER Council convenes twice a year in June and November at ITER Headquarters
First Plasma in December 2025; first scientific experiments in 2028; first nuclear plasma (DT) in 2035
The updated Schedule is challenging but technically achievable.
It represents the best technically achievable path forward to First Plasma.
Members now have all the elements needed to go through their domestic processes of obtaining approval for the Resource-Loaded Integrated Schedule
18th & 19th ITER Council endorse updated Schedule

## Slide 21
Major assembly milestones

## Slide 22
Extensive interactions among IO and DAs to finalize revised baseline schedule proposal
Schedule and resource estimates through First Plasma (2025) consistent with Members’ budget constraints
Proposed use of 4-stage approach through Deuterium-Tritium (2035) consistent with Members’ financial and technical constraints
A staged approach to DT plasma

## Slide 23
Distribution by Member
Who works for ITER?
Oct. 2017
Chart: 
| EU | CN | IN | JP | KR | RF | US
 | 0.6947 | 0.08567 | 0.034268 | 0.038941 | 0.049844 | 0.046729 | 0.049844
The international staff of the ITER Organization (Central Team) comprises ~ 800 persons (35 countries).
An equivalent number of contractors and experts are directly working for ITER in Saint-Paul-lez-Durance.
More than 2,000 specialists work for ITER throughout the world.

## Slide 24
Halfway to First Plasma
Etc.
According to the stringent metrics that measure project performance, 50 percent of the "total construction work scope through First Plasma" is now complete. More than 750 publications, from a total of 41 countries, hailed the accomplishment.

## Slide 25
Worksite progress
February 2015 – January 2018

## Slide 26
Worksite progress
February 2015 – January 2018

## Slide 27
18 January 2018
Tokamak Bdg.
Assembly Hall
Radiofrequency Heating
Cryostat Workshop
PF Coil Winding Facility
Diagnostics Bdg.
Cryoplant
400 kV Switchyard
Tritium Bdg.
Magnet Power Conversions Bdgs.
Bioshield
~ Machine axis
Service Bdg.
Cooling System
Worksite progress

## Slide 28
Assembly Hall
Before being integrated in the machine, the components will be prepared and pre-assembled in this 6,000 m2, 60-metre high building. The Assembly Hall is equipped with a double overhead travelling crane with a total lifting capacity of 1,500 tons.

## Slide 29
Load tests, both static and dynamic (1,875 – 1,650 tonnes), are now finalized in the Assembly Hall. Note the « foot » of the SSAT-1 already in place.
Assembly Hall

## Slide 30
Cryoplant
The ITER Cryoplant will be the largest single platform cryofacility in the world. It will distribute liquid helium to various machine components (superconducting magnets, thermal shield, cryopumps, etc.). The last of 18 skids supporting the helium compressors was installed atop their massive four-metre-high concrete pads in November 2017.

## Slide 31
Adjacent to the Assembly Hall, the building that will house the plasma heating systems (microwave and radio frequency) is ready to be equipped.
Radiofrequency heating
This girder is part of the gantry crane that will be used to install radio frequency and microwave heating components. It was installed in December 2017.

## Slide 32: Electrical network
The connection of the 400 kV switchyard to the French grid was successfully demonstrated on 30 March 2017.

## Slide 33
Electrical conversion
Two large Magnet Power Conversion buildings will host the transformers and converters ( AC ► DC) feeding power to the ITER magnets.
The twin buildings are now ready for equipment. Electrical components from China, Korea and Russia will be progressively installed inside of the building as well as in the exterior bays.

## Slide 34
Too large to be transported by road, four of ITER’s six ring-shaped magnets (the poloidal field coils, 8 to 24 m in diametre) will be assembled by Europe in this 12,000 m² facility.
PF Coil winding facility

## Slide 35
Manufactured in India, the 30 m x 30 m cryostat (the insulating vacuum vessel that encloses the machine) is being assembled and welded on site.
Cryostat workshop

## Slide 36: Cooling water systems
ITER power will be partly evacuated by cooling towers (procured by India).

## Slide 37
Into the industrial phase
with highly challenging specifications
Manufacturing of ITER components is taking place at the cutting edge of technology:
Geometrical tolerances measured in millimetres for steel pieces up to 17 m tall weighing several hundred tons
Superconducting power lines cooled to minus 270 degrees Celsius
Plasma facing components to withstand heat flux as large as 20 MW per m2
Cryoplant cooling capacity up to 110 kW at 4.5 K; maximum cumulated liquefaction rate of 12,300 l/hr
Etc.

## Slide 38: Who manufactures what? The ITER Members share all intellectual property
Toroidal Field coils (18)
Poloidal field coils (6)
Cryostat
Thermal shield
Vacuum vessel
Blanket modules
Feeders (31)
Divertor
Central solenoid (6)
Correction coils (18)

## Slide 39
China has successfully completed the first component of the feeder package: the cryostat feedthrough for poloidal field coil #4,
Magnet Systems, Power Systems, Blanket, Fuel Cycle, Diagnostics
Manufacturing progress
China
Work is underway in China (under contract with Europe) to manufacture 9 double pancakes for poloidal field coil # 6.

## Slide 40
European contractors have finalized 2 of 10 toroidal field coil winding packs.
Buildings, Magnet Systems, Heating & Current Drive Systems, Vacuum Vessel, Divertor, Blanket, Power Systems, Fuel Cycle, Tritium Plant, Cryoplant, Diagnostics, Radioactive Materials
The pre-production cryopump was delivred in August 2017 More than 15 companies in Europe were involved in its manufacturing,
Manufacturing progress
Europe

## Slide 41
Manufacturing progress Japan
Magnet Systems, Heating & Current Drive Systems, Remote Handling, Divertor, Tritium Plant, Diagnostics
In September 2017, the Japanese Domestic Agency and suppliers celebrated the completion of conductor fabrication; in all, 43 km (745 tonnes) of conductor were produced.
In a major production milestone the first TF winding pack has been completed at Mitsubishi Futami plant.
Similar operations are ongoing at Keihin Product Operations of Toshiba Corp.

## Slide 42
Manufacturing progress
India
Welding operations for Tier 1 of the Cryostat base are now complete. preliminary set-up for Tier 2 of the Lower Cylinder has just been completed
Cryostat, Cryogenic Systems, Heating and Current Drive Systems, Cooling Water System, Vacuum Vessel, Diagnostics
Thousands of in-wall shielding pieces have been manufactured, passed factory acceptance, and are being prepared for shipment.

## Slide 43
Manufacturing progress
Korea
On 18 December the fitting test for the first Toroidal Field Coil Structure was completed at Hyundai Heavy Industry in Ulsan. Tolerance requirements of 0.5mm +- 0.25mm were successfully met!

## Slide 44
Manufacturing progress
Russia
Power Systems, Magnet Systems, Blanket, Divertor, Vacuum Vessel, Diagnostics, Heating & Current Drive Systems
Fabrication and qualification tests of PF1 winding pack stack sample were successfully completed.
Electrical equipment prototypes were tested and qualified at the Efremov Institute in Saint Petersburg.

## Slide 45
Manufacturing progress
USA
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
General Atomics is fabricating the 1000-ton Central Solenoid (CS). In April 2016, winding of the first CS module was completed.
Module tooling stations are in place and being commissioned, including the heat treatment furnace shown here.

## Slide 46
Manufacturing progress
USA
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
The turn insulation station wraps each bar of conductor
with Kapton® fiberglass tape.
The top plate of the central solenoid assembly platform during fabrication at Robatel.

## Slide 47
Manufacturing progress
USA
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
Forging of a tie-plate first article. The tie-plates are part of a substantial structural cage surrounding the central solenoid magnet.
After forging, the tie-plates are machined to required specifications.

## Slide 48
Manufacturing progress
USA
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
The cryoviscous compressor full-scale prototype was successfully tested at the ORNL Spallation Neutron Source cryo facility.
A roots pump prototype has been successfully tested at ORNL.

## Slide 49
Manufacturing progress
USA
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
A blower for cooling transmission lines will be tested on the high-powered ORNL resonant test line.
A radio-frequency discharge system for diagnostic mirror cleaning is in development and testing. [Inset: Electron cyclotron emission prototype developed at General Atomics and tested on DIII-D.]

## Slide 50
Manufacturing
progress
Cooling Water System, Magnet Systems, Diagnostics, Heating & Current Drive Systems, Fuel Cycle, Tritium Plant, Power Systems
The US has delivered an array of components for the steady state electrical network and completed deliveries in 2017.
USA

## Slide 51
Unloaded at Marseille industrial harbour, components are ferried through the inland sea Etang de Berre on a specially designed barge and delivered to ITER by way of the 104-km long “ITER Itinerary”. The journey to the ITER site takes 3 to 4 nights.
Door-to-door delivery
62 Highly Exceptional loads (HEL) delivered as of Jan. 2018
214 expected before 2025 - 18 expected after 2025

## Slide 52
The 104-km long ITER Itinerary between Berre-l’Etang and the ITER site is part of France’s contribution to the ITER project.
The ITER Itinerary

## Slide 53
Economic benefits
$ 8 billion is currently engaged in construction and manufacturing contracts for ITER worldwide
ITER

## Slide 54
Engaging US industry, universities and national laboratories
Economic benefits (US)
As of September 2017, over $957M has been awarded to US industry and universities and obligated to DOE national laboratories in 44 states plus the District of Columbia. To complete its contributions to ITER, the project anticipates an estimated $800M in future contracts to US industry.
Note: This data does not reflect contracts awarded to US industry by the EU (>$55M).
> $ 20M
$ 1M – 20 M
< $ 1M

## Slide 55
Key contracts and awards
US ITER contracts have been awarded in 43 states + D.C.
General Atomics, San Diego, CA; Central solenoid modules
AREVA Federal Services, LLC, Charlotte, NC; Tokamak cooling water system design and drain tank fabrication
Luvata Waterbury, Inc., Waterbury, CT; Toroidal field conductor strand
Transproject, Houston, TX; Shipping
Oxford Superconducting Technology, Carteret, NJ; Toroidal field conductor strand
High Performance Magnetics, Tallahassee, FL; Toroidal field conductor integration/jacketing
Massachusetts Institute of Technology (MIT), Cambridge, MA; Magnet systems and electron cyclotron transmission lines support
Hyundai Corporation, Houston, TX; Steady state electrical network HV transformers
New England Wire Technologies, Lisbon, NH; Toroidal field cabling services
ABB, Raleigh, NC; Steady state electrical network
Siemens Industry, Inc., Wendall, NC; Steady state electrical network control & protection
Peterson, Inc., Ogden, UT; Central solenoid structures
CPI Microwave Power Products, Palo Alto, CA; Gyrotron for electron cyclotron transmission lines R&D
Eaton Corporation, Cleveland, OH; Steady state electrical network switchgear
Major Tool & Machine, Inc., Indianapolis, IN; Central solenoid structure tie plate prototype
Pfeiffer Vacuum, Nashua, NH; Roughing pump
Inficon, Inc., E. Syracuse, NY; Vacuum leak detectors
G&G Steel, Russellville, AL; Central solenoid structure tie plate prototype
Mega Industries, LLC, Gorham, ME; Ion cyclotron heating support
Dielectric Communications, Raymond, ME; Ion cyclotron heating support

## Slide 56
Meeting milestones and more
Full paced construction and manufacturing
All (30) milestones now achieved through 4th Quarter 2017
Approval of Overall Project Schedule by ITER Council
Approval of Overall Project Cost ad referendum
Promotion of ITER-wide project culture
  Success requires full commitment by each person
Measures of progress and uncertainties
ITER Member support for the project
OPC approved or on the way to be approved by six ITER Members
USA: approved US OPC on Jan. 2017;
  Briefing of Congressional Committee: strong expressions of support
  Briefing of new DOE Secretary Rick Perry in April and Oct. 2017
  Insufficient budget in 2016-2017; 2018 and 2019 ?
UK: positive expectation for continuing UK participation in ITER
  Article 50 negotiations beginning; positive remarks by UK government
  UK delegation visited ITER recently to view project and meet with staff

## Slide 57
Challenges ahead for ITER
until construction completion
ITER Organization, Domestic Agencies and suppliers working as “One-ITER Team” with a strong project culture
Strict respect by suppliers for quality and safety requirements
Strict respect by all stakeholders for the schedule requirements, in particular for the required delivery dates for materials and equipment on the ITER site
Reliable and fully integrated assembly/construction sequences on ITER site
Contracting with high performing and experienced companies for the assembly activities in the Tokamak Complex
Setting in place a well-suited organization in charge of commissioning
Setting in place a well-suited organization to conceive and execute the progressive take-over of the machine, ultimately for its operation and maintenance
Timely, reliable availability of the planned and committed resources from the seven ITER Members

## Slide 58
ITER is moving forward!
http://www.iter.org
Thank you for your attention