## Slide 1: The Science of ITER

## Slide 2: Inside the Tokamak Building

## Slide 3: The ITER Tokamak
Vacuum Vessel: ~ 8 000 t.
TF Coils: ~ 18 x 360 t.
Central solenoid: ~ 1 000 t.
Total ~ 23 000 t.
R = 6.2 m, a = 2.0 m
B = 5.3 T, I = 15 MA

## Slide 4: What Is the Mission of ITER?
Quoting from the Project Specification (‘the top level ITER Technical Document’):
…demonstrate the scientific and technological feasibility of fusion energy for peaceful purposes
But how?

## Slide 5: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 6: Why These Conditions?
Fusion power of ~500 MW is the minimum for a power plant
Q ~ 10 is the minimum for a power plant; also dominant self-heating
Stationary conditions imply duration is not limited by physics, but hardware investment
Direct comparison of inductive and steady-state scenarios in burning plasmas answers a key design question for the next step
Wide parameter range requirement avoids a ‘point solution’
Minimum cost because … why pay more?
In the following, I would like to explore the science of these—the ITER design basis and in turn what science questions will be answered

## Slide 7: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 8: 500 MW Fusion Power
Fusion power for DT reactions is given by (in the range where <sv>  T2):
Pfus (MW) ≈ 7.6 10-12 p2 V
Therefore, smaller devices need higher pressures to reach the 500 MW goal
  Pressure can be limited by MHD stability or confinement
<sv> T2

## Slide 9: MHD Stability Pressure Limits
MHD equilibrium is given by:
p = j x B = ( x B) x B/m0
There is a dimensionless parameter 2m0p/B2, which is the ratio of thermal to magnetic energy (b) and is << 1
In a tokamak, the following parameters are also small: r/R and BP/BT  I/aBT
With 3 small parameters, ratios yield two O(1) parameters: i = 1/q = RBP/rBT and b/(I/aBT), which describe limits on current and pressure in ideal MHD, predicted by theory and validated by experiment

## Slide 10: Pressure Limits and Fusion Power
Adding the stability scaling gives:
Pfus (MW) ≈ 2.9 10-2 (f I B)2 Rk
  f is the fraction of the maximum pressure limit
For a given operating scenario, I  B and f is constant, so fusion power rapidly increases with B => choose highest practical B
Tokamak scenarios can trade f and I to give the same fusion power
  ITER baseline has max(I) and f ≈ 0.5 to lower risk of instability, including tearing modes
  Other scenarios can have same f x I at lower I => want to explore a wide operating space
G Huijsmans, JET
JET

## Slide 11: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 12: Gain (Q) Is Determined by Confinement
For DT fusion, 20% of the fusion power goes to a particles and can heat the plasma
At the 500 MW operating point, 100 MW of self-heating power is available and Q ≥ 10 implies the auxiliary heating power is ≤ 50 MW
Reaching 500 MW fusion power implies two conditions:
  The available power can heat the plasma to the required pressure
  The self-heating is effective

## Slide 13: Gain (Q) Is Determined by Confinement
As tokamaks are heated, stored energy increases more slowly than linear with power
  Stored energy/Input power = Confinement time
  Transport is characterized by the ratio of flux to gradient
At a certain power, the plasma transitions spontaneously to very low transport of particles and heat at the edge (H-mode)
  PLH (MW) = 0.098 mH-1 B0.80 n0.72 S0.94
  In ITER, the plasma should be ~5 keV very near the plasma boundary => good fusion reactivity in the entire volume
  Sufficient power must be applied to sustain this edge condition
Plasma Pressure
H mode
L mode
Early DIII-D work

## Slide 14: How Is Tokamak Confinement Predicted?
Three main methods are used to predict energy confinement:
  Engineering parameter scaling
  Dimensionless physics parameter scaling
  Direct numerical solution of the fundamental equations
Each of these methods has strengths and weaknesses
To predict gain, it is necessary to get self-consistently the pressure (related to stored energy and the self-heating) and the additional power needed to reach that pressure

## Slide 15: Engineering Parameter Scaling
Database of confinement time from many tokamaks fit by linear regression to a power law dependence on engineering parameters
Strengths:
  3 orders of magnitude in fit extrapolated to target less than 1 order outside the data
  Easily used for large design surveys
ITER
Weaknesses:
  Improper linear regression
  Burning plasmas enter a regime of significant intrinsic radiation (esp. cyclotron radiation)
E  I R2 P-2/3

## Slide 16: Dimensionless Parameter Scaling
Use similarity arguments to reduce the number of scaling parameters to two
  Can keep shape, b, and q fixed
  Two other dimensionless parameters: number of gyroradii across the plasma, number of transits before a collision
JET
DIII-D
C-Mod
Strengths:
  Variables from basic physics
  Validated by identity experiments
Weaknesses:
  Uncertainties large => cannot be used alone for prediction, but can be used to check scalings

## Slide 17: Direct Numerical Solutions
The fundamental equations governing the plasma turbulence are believed to be known
  Modern computers can now solve these for realistic parameters
Strengths:
  First-principles physics
Weaknesses:
  Not practical for design optimization, but can check design points
  Solutions sensitive to boundary conditions that do not have the same first-principles basis

## Slide 18: Self-Heating of Plasmas is a New Regime
The charged fusion product of DT reactions is a 3.4 MeV a particle
  First time plasmas are heated by an isotropic particle distribution in velocity space
  Most calculations all a particle is thermalized except prompt losses
These a particles are faster than the phase velocity of Alfvén waves in the background plasma
Fuel mixture:
Depletion:
Drive from alpha-particles + beams
Damping from thermal plasma
The wave-particle interaction can lead to instability
  Waves excited are eigenmodes of the background plasma
  Think of Cherenkov emission in an active medium where gain is possible

## Slide 19: Plasma Response is Also in a New Regime
From dimensionless parameter arguments, the toroidal wavelength of the most unstable modes is proportional to the number of gyroradii across the plasma radius
  NSTX: n≈1, DIII-D: n≈3-5; ITER: n≈15-25
The background particles in ITER will see a wave field more typical of turbulence than discrete wave fields
Calculations indicate little loss of heating efficiency due to a particle transport
  But we have to actually test it!

## Slide 20: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 21: Reaching Stationary Conditions
Four significant issues must be dealt with to reach stationary conditions:
  Supplying the magnetic energy associated with the operating current
  Handling of the stationary heat and particle exhaust (focus on heat here)
  Eliminating the transient heat loads associated with standard H-mode operation
  Stable stationary operating scenarios must be realized
Each of these has fundamental implications for the design of a burning plasma device

## Slide 22: Supplying the Magnetic Energy
A fundamental design consideration for any tokamak is the inner ‘radial build’—the space required for the toroidal field coils, solenoid, and (for burning plasmas) blankets and shielding
  There is no demonstrated method to remove completely the need for a solenoid for the current rise, even if it is not needed for sustaining the plasma
  To achieve stationary conditions, the plasma duration should be at least 2 current relaxation times for any scenario
  The magnetic stored energy required to reach maximum current is far larger than than dissipated by resistivity in current flattop for 2 current relaxation times
ITER solution: >270 Wb of flux, more than 200 Wb is needed to get to 15 MA
  Lower current pulses can then be run substantially longer (up to 3000 s)

## Slide 23: Handling Heat and Particle Flux
Power load [MW/m2]
Rolls Royce Trent 900
Re-entry
vehicle
ITER transients
Ariane 5/
Vulcain 2
HWR
ITER steady-state
~1 <10 85 2000
Arc welding
The challenge is not small!

## Slide 24: The First Challenge: How Big is the Problem?
The thickness of the layer in which heat is exhausted is small (few mm)
  ITER design assumption was ~3-4 mm based on stability considerations
Recent empirical scaling would extrapolate to 1 mm!
  Scaling is consistent with an analytic model based on particle drifts
State-of-the-art numerical solutions indicate turbulence in ITER should broaden the exhaust layer to ~5 mm
  Existing machines cannot reproduce these conditions
PSOL ~120 MW
Power flow

## Slide 25: The Second Challenge: How to Handle the Problem?
To reduce the heat flux, deliberate introduction of impurities, such as noble gases, is envisioned
Preferably, radiation is in the main chamber to spread the energy over a larger surface
  Potential problem with dilution from impurities entering the core plasma
  Potential problem staying in H mode if too much power radiates from the core plasma
Many experiments have demonstrated radiation in the divertor in order to ‘detach’ the field lines from the divertor targets
  The radiating zones and the area over which the energy is deposited may be too small
Dissipation zone
SOL
PSOL
b
lq

## Slide 26: The Third Challenge: How to Compute the Problem?
Present calculations contain many of these effects, but are not yet comprehensive
Present-day tokamaks cannot reproduce the ITER divertor conditions
SOL
PSOL
b
lq

## Slide 27: Transients in Standard H-Mode: ELMs
ASDEX-Upgrade
E. Wolfrum
The high confinement at the plasma edge in H mode is actually too high
  Pressure increases until an instability limit is reached
In present-day tokamaks, this has beneficial effects
  Particle content of the plasma can be controlled by pumping
  Impurity content of the core is reduced

## Slide 28: Single ELMs Might Cause Melting
Scaling of the energy loss in large ELMs projects energy near the surface melt limit of the ITER divertor
T. Eich et al., [39]
JET-C
JET-ILW
AUG-C
AUG-W
MAST
ITER-Regr.
AUG-W-inner
*
T. Eich, Nucl. Mater. Energy (2017)
~ surface melt limit
ITER 7.5, 15 MA

## Slide 29: Mitigation of ELMs
The primary method for ELM mitigation in ITER is application of Resonant Magnetic Perturbations
  This has been successfully applied in several tokamaks
  ITER can apply up to n=4
In addition, a pellet system to trigger ELMs at a pace much faster than natural will be available

## Slide 30: What About Disruptions?
A very important reason to operate stationary discharges in ITER is to end the concern about disruptions
  A truly stationary plasma will not disrupt because of plasma physics
  Disruption occurrence should become a component or power supply reliability issue and not a physics issue
The key question is whether truly stationary operating scenarios exist
  Note: take care that stationary ≠ steady-state

## Slide 31: Do Candidate Stationary Scenarios Exist?
ITER baseline scenario operated stably at zero input torque in DIII-D
Advanced inductive scenario operated at low torque JT-60U to 28 s
DIII-D

## Slide 32: Disruption Mitigation Is Still Mandatory
Mitigation pellets are substantially larger than ordinary fuelling pellets (leftmost)
13 mm
20 mm
17 mm
28 mm
ITER must be ready to mitigate disruptions at any operating point
  Learning to run a stationary discharge will not happen in a day
  Components and power supplies will fail

## Slide 33: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 34: True Steady-State Scenario Will Be Difficult
With the day-1 heating and current drive systems, fully non-inductive operation predictions range from Q=2-5
  Even with upgrades, true steady-state scenario is difficult because of divertor heat loads at reduced density
However, ITER can definitively compare scenarios with different q profiles proposed for steady-state operation
Two key aspects of the comparison:
  Dependence of energy confinement on q
  Dependence of stability of Alfvén modes excited by fusion a particles as a function of q

## Slide 35: Physics, Engineering, and Operational Objectives Were Specified
Achieve fusion power of 500 MW with Pfus/Pin ( Q) ≥ 10 for 300-500 s (i.e., stationary conditions)
Aim at demonstrating steady-state operation with Q ≥ 5
Capable of advanced operational modes and a wide operating parameter space
Achieve the minimum cost device that meets all the stated requirements

## Slide 36: What Questions Will ITER Answer?
While we are are confident in the design basis for ITER, it is still an experiment
  This means operation of ITER as envisioned in the design basis will validate (or invalidate) its design basis
In the time between now and ITER plasma operation (and especially DT operation), simulation capability will continue to advance
  This means operation of ITER will validate (or invalidate) the physics and assumptions in a variety of simulations

## Slide 37: Fusion Questions ITER Will Answer
By design, ITER will answer several key questions for fusion energy, such as:
Does self-heating work?
How large does a plasma need to be to achieve dominant self-heating?
Are advanced scenarios actually ‘advanced’?
Is steady-state operation feasible in a burning plasma?
Is there a self-consistent solution coupling a burning core plasma to a working heat and particle exhaust solution?
Can helium ash be exhausted?
Are plasmas disruption-free in stationary conditions?

## Slide 38: Physics Questions ITER Will Answer
ITER will address several interesting plasma physics questions, such as:
Does gyro-kinetic theory really describe plasma transport?
What limits the inverse cascade of turbulent energy at low wavelength?
Is there ‘intrinsic’ rotation?
Do heat and particle transport depend strongly on gyroradius or collision frequency?
What is the mechanism of the L-H transition?
What is the mechanism for runaway generation in a disruption?
Are high temperature plasmas more or less prone to tearing modes?
Do current drive efficiencies increase with temperature?
What is the origin of isotope scaling?

## Slide 39: When Will ITER Answer These Questions?
ITER will can address some questions in the early operational phases, but system commissioning for DT is the highest priority task

## Slide 40: ITER Hardware Availability

## Slide 41: Disruption Physics and Mitigation
Disruption mitigation is necessary from early in PFPO-1
  Validity of scaling projections for the mitigation will be immediately known
Operation at full field will be done in PFPO-1 specifically to test the scaling of runaway generation with B

## Slide 42: Other Physics Issues Addressed in PFPO
Size scaling of L mode in hydrogen
Current and size scaling of the scrape-off layer power width in L mode
L mode divertor detachment
Fueling physics
H-mode transition and confinement scaling with size
Error field sensitivity and correction
Intrinsic rotation
…

## Slide 43: ITER Will Be The First Look At Burning Plasma