## Slide 1: Chemical Neutralization Applications in Demilitarization of Conventional Munitions October 24, 2017
Presented to:
Committee on Alternatives for the Demilitarization of Conventional Munitions (CMD Committee)
National Academy of Sciences
Washington DC. USA
Presented by:
Valentine Nzengung, PhD Professor University of Georgia
3675 Crestwood Parkway Atlanta, GA 30096
www.munirem.com
vnzengung@munirem.com

## Slide 2: Presentation Outline
Introduction to MuniRem™ technology
Demonstration/validation test for bulk explosives
Full scale chemical neutralization of bulk explosives
Chemical neutralization of bulk explosives abandoned on demilitarization equipment
On-site demilitarization of recovered underwater munitions
Chemical destruction of chemical warfare materiel (CWM)
Incorporation of MuniRem solution into existing demilitarization systems
MuniRem technology rating and summary

## Slide 3: Introduction to Munirem Technology

## Slide 4: Chemical Neutralization of Energetics
Chemical Oxidation
  Alkaline Hydrolysis
  Activated Persulfate
  High Temperature Oxidation
Chemical Reduction
  MuniRem
  Nano Zero Valent Iron (nZVI)

## Slide 5: What is MuniRem?
MuniRem is the commercial name for a University of Georgia Research Foundation patented technology that employs reduction chemistry to rapidly neutralize and destroy explosives and energetics in different media.
The end product is non-hazardous.
MuniRem also degrades chemical warfare materiel (CWM) and stabilizes metals.
MuniRem is licensed exclusively to MuniRem Environmental, LLC

## Slide 6: Types of Explosives Neutralized and End Products
Effective in Neutralization and Remediation of
Mustard (CWA)
HMX / RDX / TNT
DNTs / ADNTs
NBs / NDMA
Nitrocellulose Propellant
PBX / PETN PCBs Lead Styphnate Lead Azide Picric Acid AN/TATP
Reactive Aluminum
As, Ba, Cd, Cr, Pb, Hg, etc.
The MuniRem reagent is versatile in its ability to neutralize a variety of energetics

## Slide 7: Effect of MuniRem reagent on Heavy Metals

## Slide 8: Multiple Evaluations at Bench & Pilot Scale
University of Georgia
Orbital ATK Laboratory, LCAAP
Army Laboratory, Vicksburg, MS
NDCEE/AEC Independent Evaluation, Pennsylvania
Non-Stockpile, Edgewood, MD
Indian Head (NAVFAC)
SMS

## Slide 9: Demonstration/Validation Test for Bulk Explosives
Evaluation of MuniRem efficacy for the neutralization of bulk explosives
Contract # W912PP-09-P-0125

## Slide 10: Options for Recovery of Bomb Fillers (Bulk Energetics)
Water jet
Water saw
Milling
Cryogenic Breaching
Projectile Casings
Recovered Bulk Energetics
Breaching and Recovery of Bulk Energetics

## Slide 11: Custom Built Neutralization Reactor for Bulk Energetics
Waterjet breaching of Navy Projectiles
100 gallons neutralization tank
10 Lbs explosive per batch
Manual loading of explosives
Reaction time < 1 hour
Polishing column – packed bed reactive media

## Slide 12: Chemical Neutralization of Recovered Bulk Explosives (schematic)

## Slide 13: Pilot Scale Demonstration Neutralization of Multiple 10 lb Batches of Bulk Explosives
Custom Built Explosive Neutralization Reactor
Neutralization in under 30 minutes
Effluent wastewater target of 2 ppm explosives
Decontaminated casings to MDAS
Non-hazardous wastewater
Water recycling and re-use

## Slide 14: Pilot Scale Results: Neutralization of Multiple 10-Lb Batches of Composition D
Batch # | Initial Conc’n (mass) | Conc’n in Effluent of Neutralization Reactor | Conc’n after Polishing Column | % Neutralized in Reactor | % Removal Effluent of Polishing Column
T0 | 1400 mg/L (1 lb) | 602 mg/La | 9 mg/La | 57.00% | 99.36%
T1 | 14,000 mg/L (10 lbs) | 3200 mg/Lb | 920 mg/Lb | 77.14 % | 93.43%
T2 | 14,000 mg/L (10 lbs) | 540 mg/Lb | 550 mg/Lb | 96.14% | 96.07%
T3 | 14,000 mg/L (10 lbs) | 24 mg/Lb | 2.2 - 9.9 mg/Lb | 99.83% (Optimized) | 99.93 %
Note: a = onsite detects; b = confirmatory results from TestAmerica (single detect or highest from multiple detects)

## Slide 15: Full Scale Chemical Neutralization of Bulk Explosives

## Slide 16: Scale-up Option Small Scale Demilitarization (Schematic)

## Slide 17: Industrial Scale Demilitarization Chemical Neutralization Facility (Schematic)

## Slide 18: Thermal Vs. Non-thermal Decontamination
Thermal Decontamination
MuniRem Bath Decontamination

## Slide 19: Large Scale Decontamination of Demil Scrap Metal (schematic)

## Slide 20: Chemical neutralization of bulk explosives abandoned on demilitarization equipment
Camp Minden, Louisiana

## Slide 21: Abandoned Bulk Explosive Neutralization
Melter/Flaker machine contained bulk H-6 (TNT, RDX, AL, Binder) explosives
Large crystallized chunks of H-6 on equipment
Wall surfaces and miscellaneous materials contaminated with explosives
Lead paint chips mixed in with explosives

## Slide 22: Small Footprint of MuniRem Solution Application
Explosives Neutralization Station Behind Building

## Slide 23: MuniRem Solution Provided Safe Recovery of Crystallized Explosives
Large H-6 chunks safely removed while spraying MuniRem solution
Large explosive pieces transferred to neutralization reactor
Neutralization of recovered explosives achieved rapidly in reaction tanks

## Slide 24: Neutralization of Recovered Explosives
2,000 Lbs of H-6 explosives estimated as present on and in equipment
>1000 lbs destroyed in place by spraying concentrated MuniRem solution
>900 lbs recovered and neutralized on-site in reactor with MuniRem solution
Sludge and wastewater characterized as non-hazardous waste

## Slide 25: On-site Demilitarization of Underwater munitions
MuniRem supports Savannah Harbor Expansion Project (SHEP)

## Slide 26: CSS Georgia Background
Ironclad gunboat built for the Confederacy in 1862
Completed Vessel was too heavy
CSS Georgia spent her life as a floating battery in what is now the north edge of the Savannah Harbor navigation channel
CSS Georgia scuttled by Confederate troops on December 24, 1864
Recovery of CSS Georgia and its munitions part of Savannah Harbor Expansion Project

## Slide 27: On-Site Neutralization of Munitions Recovered from Underwater Environment: Savannah River Harbor Expansion Program

## Slide 28: Breaching of Recovered Projectiles Total projectiles breached and neutralized = 170
Breaching throughput = 12 projectiles per hour

## Slide 29: Neutralization of the Breached Munitions
After 150 years explosives still well preserved
Explosives washout using MuniRem solution
Explosives neutralized
Fuzes safely removed and inerted
Munitions certified by SUXOS as safe
Characterization and disposal of non-hazardous waste

## Slide 30: Summary – Underwater Munitions Demilitarization
170 Civil War munitions neutralized on-site in 2015
Munitions transferred to U.S. Army Corps
Munitions preserved for historical purposes
No hazardous waste produced
Largest on-site neutralization of recovered underwater Confederate munitions
Follow up project November 2017
Inerted Fuze

## Slide 31: Chemical Destruction of Chemical Warfare materiel (CWM)
Contract #: W912PP-10-P-0034
Results presented are obtained from proof-of-concept test data for tests conducted at Non-Stockpile laboratory, Edgewood (2010)

## Slide 32: CWM Deactivation/Neutralization Approaches
Baseline Incineration
Superchlorinated bleaches - solution or powder
Anionic Oxidation
Supercritical Water Oxidation
Electrochemical Oxidation
Donovan Chamber – TC-25
Hydrolysis – hydrolysis of larger amounts of HD (>0.1 M) is a reversible process.
Explosive Destruction System (EDS)
MuniRem

## Slide 33: Criteria for Effective Neutralization of CWAs
Reagent should be stable over a wide range of temperatures
Effective over a wide pH range or stabilized with a buffer
Fast acting – possible free radical mediated reactions
Irreversible reactions
No toxic degradation products

## Slide 34: Disadvantages of Mustard Hydrolysis
Hazardous end-product
Mustard undergoes reversible hydrolysis reactions
High upfront capital investment

## Slide 35: Degradation of Mustard Mediated by Sulfoxyl Free Radicals
Activated Persulfate (SO4-•)  Chemical Oxidation
Activated hydrosulfite (SO2-•)  Chemical Redcution

## Slide 36: Tests at Lawrence Livermore National Laboratory
Title: “Direct Chemical Oxidation: Applications to Demilitarization and Decontamination”
Performers: John F. Cooper; Bryan Balazs; Patricia Lewis
CWA Treated: “one-armed mustard” gas - thiodiethanol [(OHH2CCH2)2-S] and dimethylsulfoxide [(CH3)2-SO], non-toxic surrogates for hydrolyzed Mustard gas.
Chemical Reagent: Oxidation at 90oC using peroxydisulfate (persulfate) solutions.

## Slide 37: The Chemistry of Mustard Favors Abiotic Degradation by MuniRem
Thioethers are characterized by C-S-C bonds. The C-S bond is both longer, because S is larger, and weaker than C-C bonds.
The bond dissociation energies for dimethyl sulfide and dimethyl ether are respectively 73 and 77 kcal/mol (305 and 322 kJ/mol).
Formulations of MuniRem dissociate C-C bonds in chlorinated ethenes and nitroatomatics

## Slide 38: Results from Proof-of-Concept Evaluation Study Titled MICRO-SCALE EVALUATION OF MuniRem REAGENTS FOR THE DEMILITARIZATION OF SULFUR MUSTARD
MuniRem reagent evaluation was independently performed by the United States Department of Defense at its Non-Stockpile Department, Edgewood, MD.

## Slide 39: Rate of Degradation of HD by MuniRem Reagent vs. Rate of Reversible Hydrolysis of HD by Water
Initial = 40 uL (9,000 mg/L)
Initial = 60 uL (14,000 mg/L)
Initial = 80 uL (18,500 mg/L)
MEA forms Hazardous Waste

## Slide 40: Neutralization of Mustard (HD) with MuniRem Reagent
3 Hours
6 Hours
1 Hour
Nothing = Homogeneous Solution of MuniRem; no solids added.
Sand and Metal (Iron) was added to simulate reality
Initial Concentration of Mustard = 18,500 mg/L
Results for: 1 hour; 3 hours; 6 hours

## Slide 41: Evidence of Mustard (HD) Destruction by MuniRem Ethylene Production as a Function of Time

## Slide 42: Quantitative Measurements of Ethylene End-Product in the Headspace of MuniRem Treated Mustard (HD)
Nothing = MuniRem Solution Only
Sand = MuniRem solution + Sand as Impurity
Metals = MuniRem solution + Metals (Fe oxides) as Impurity
Metals = MuniRem solution + Sand & Metals as Impurity

## Slide 43: Formation of Ethylene from Mustard (HD)
Reductive Dechlorination
Catalyzed by MuniRem
CH2=CH2 + S2- (formation of metal sulfide )

## Slide 44: Incorporation of MuniRem into existing demilitarization systems

## Slide 45: MuniRem Chemical Agent Neutralization Process
CW Munitions Moved from Storage
Chemical agent separated from shells or casings
CWM in EDS reactor
Shells or casings soaked in MuniRem bath
Water & MuniRem
CWM destroyed with MuniRem to Ethylene gas, chloride & sulfide
Sampling & analysis of treated waste
Shells or casings decontaminated
Shells or casings Rinsed with water
Waste analyzed & discharged as non-hazardous waste
Treated waste discharged as non-hazardous waste

## Slide 46: Further Development of MuniRem Technology for Use in Explosive Destruction System (EDS)
Evaluation of optimized MuniRem reagent
Pilot test in EDS
Obtain needed approvals

## Slide 47: Schematic of Closed Loop Decontamination of One Ton Steel Containers

## Slide 48: MuniRem Rating and Summary

## Slide 49: MuniRem Technology Rating
No. | Criteria | Rating
1 | Maturity | Already applied at full scale to demilitarize discarded military munitions and neutralize bulk explosives Compliments other demilitarization technologies
2 | Process Efficacy | Demonstrated and validated at bench, pilot and full scale
3 | Process Throughput | 10s to 100s pounds per hour. Determined by breaching and neutralization method
4 | Process Safety | Very safe. Near instant neutralization of most energetics
5 | Public & Regulatory Acceptance | Already approved on multiple State and Federal projects
6 | Secondary Waste Issue | Not a concern
7 | Destruction Verification Capacity | Available and Rapid. EXPRAY Test Kits and similar commercially available wet chemistry explosives sensors
8 | Process Flexibility | Very scalable and adaptable. Easily transportable for on-site demilitarization. Fixed facility not a requirement for application

## Slide 50: Summary
MuniRem solution is versatile in its ability to neutralize a variety of energetics and chemical warfare agents.
The reaction of MuniRem reagent with bulk explosives is vigorous but not violent.
MuniRem solution is easily coupled with munitions breaching methods: waterjet cutting, milling, water saw cutting, steaming, shaped charge & cryogenic fracturing.
MuniRem solution treats the waste stream of waterjet and water saw cutting of munitions.
MuniRem solution increases throughput of EDS and similar demilitarization technologies.

## Slide 51: MuniRem is a safe, well-proven technology that should be part of every project requiring munitions destruction